Metastability problems commonly occur when a signal is transferred between circuitry in unrelated or asynchronous clock domains

- The first register in the new clock domain acts as a synchronization register.
- The registers in the chain are all clocked by the same or phase-related clocks
- The first register in the chain is driven from an unrelated clock domain, or asynchronously
- Each register fans out to only one register, except the last register in the chain

- If you are switching the control signal from one clock domain to the other, use a d flip flop. If you are sending a data bus, use DCFIFO.
- MTBF, due to metastability provides an estimate of the average time between instances when metastability could cause a design failure.

- The C1 and C2 constants depend on the device process and operating conditions.