## Slide 1: A Review of 1076 - 2019 IEEE Standard for VHDL
by Furkan Kaya, Koray Karakurt,
Mert Ecevit, Orhan Çalışkan, Seyit Koçak and Yunus Küçük
11/01/2025

## Slide 2
3.1 General
3.2 Entity Declarations
3.3 Architecture Bodies
3.4 Configuration Declarations
3. Design entities & configurations
Chapter 3
Presenter:
Furkan Kaya

## Slide 3
3.1 GENERAL
3.2 ENTITY DECLARATIONS | 3.3 ARCHITECTURE BODIES | 3.4 CONFIGURATION DECLARATIONS
Design Entity:
  Entity declaration
  Architecture bodies
  Configuraiton decleration
An entity in VHDL defines the external interface of a design.
entity full_adder is
port ( x, y, cin: in bit;
cout, sum: out bit
);
end full_adder;
entity andgate is
generic (
n: natural := 2
)
port(
inputs : in bit_vector (1 to n);
result : out bit
);
end entity andgate;
entity testbench is
end testbench;
An architecture in VHDL describes the internal implementation of an entity.
architecture behavioral of sensor_cntrllr is
component i2c_master is
...
end component i2c_master;
constant por_lim : integer := 99_999;
type sensor_states is (
por_wait, cfg_sensor, take_data, bft_wait
);
signal sensor_ctrl_state : sensor_states;
signal por_cnt : integer range 0 to por_lim;
begin ...
A configuration in VHDL specifies how components within an architecture are bound to entities and architectures.
library ttl, work;
configuration v4_27_87 of processor is
use work.all;
for structure_view
for a1: alu
use configuration ttl.sn74ls181;
end for;
for m1,m2,m3: mux
use entity multiplex4 (behavior);
end for;
for all: latch
-- use defaults
end for;
end for;
end configuration v4_27_87;
Examples 1 and 3 taken from "IEEE1076-2019" document where example 2 is my example.
EX-1
EX-3
EX-2

## Slide 4
4. Subprograms & packages
4.1 General
4.2 Subprogram Declarations
4.3 Subprogram Bodies
4.4 Subprogram Instantiation Declarations
4.5 Subprogram Overloading
4.6 Resolution Functions
4.7 Package Declarations
4.8 Package Bodies
4.9 Package Instantiation Declarations
4.10 Conformance Rules
Chapter 4
Presenter:
Seyit Koçak

## Slide 5
Subprograms define algorithms through procedures and functions, serving to compute values or perform actions
Procedures are subprograms that execute a series of statements to perform actions but do not return a value, they are called as statements and can modify the state of the program
Functions are classified as pure or impure
Packages separate the declarations and bodies of these subprograms, allowing common resources to be shared
4.1 GENERAL
4.2 SUBPROGRAM DECLERATIONS
Subprogram declarations define procedures or functions by specifying their designator, parameters, generics (if any), and for functions, the return type and whether it is pure or impure
Procedures are always identified by a name, while functions can also be identified by operator symbols, enabling operator overloading
Functions return a value, whereas procedures execute actions without returning any value and can modify external variables or signals

## Slide 6
CODE EXAMPLE
library IEEE;
use IEEE.std_logic_1164.all;
use IEEE.numeric_std.all;
entity procedurewithclock is
port (
clk : in std_logic;
reset : in std_logic;
data_in : in std_logic_vector(7 downto 0);
data_out : out std_logic_vector(7 downto 0)
);
end procedurewithclock;
architecture behavioral of procedurewithclock is
procedure updatevalue(
signal clk : in std_logic;
signal reset : in std_logic;
signal data_in : in std_logic_vector(7 downto 0);
variable data_out : inout std_logic_vector(7 downto 0)
) is
begin
if reset = '1' then
data_out := (others => '0');
elsif rising_edge(clk) then
data_out := data_in;
end if;
end procedure;
begin
process(clk, reset)
variable temp_data : std_logic_vector(7 downto 0);
begin
updatevalue(clk, reset, data_in, temp_data);
data_out <= temp_data;
end process;
end behavioral;

## Slide 7
4.2 SUBPROGRAM DECLARATIONS (continues)
Pure functions always return the same output for the same input values
Impure functions may produce different outputs for the same inputs or modify external variables or signals
Constant parameters allow read-only access, while variable parameters allow both reading and writing of values during subprogram execution
Signal parameters pass references to signals, their drivers, or both into the subprogram call
4.3 SUBPROGRAM BODIES
A body consists of three main parts: specification (definition of parameters and type), declarative part (variables, constants, or nested subprograms), and statement part (sequential operations)
4.4 SUBPROGRAM INSTANTIATION DECLARATIONS
Subprogram instantiation customizes a general subprogram template into an independent version with specific parameters or generics

## Slide 8
CODE EXAMPLE
library IEEE;
use IEEE.std_logic_1164.all;
use IEEE.numeric_std.all;
package my_subprograms is
function add_integer(a, b: integer) return integer;
end my_subprograms;
package body my_subprograms is
function add_integer(a, b: integer) return integer is
begin
return a + b;
end add_integer;
end my_subprograms;
use work.my_subprograms.all;
entity subprogram_instantiation_example is
port (
a_in, b_in : in integer;
c_in, d_in : in integer;
result_int : out integer;
result_real: out integer
);
end subprogram_instantiation_example;
architecture behavioral of subprogram_instantiation_example is
constant threshold : integer := 10;
begin
process(a_in, b_in, c_in, d_in)
variable temp_result_int : integer; --temporary storage
variable temp_result_real : integer;
begin
if (a_in > threshold and b_in > threshold) then
temp_result_int := add_integer(a_in, b_in);
result_int <= temp_result_int;
else
result_int <= 0;
end if;
if (c_in > threshold and d_in > threshold) then
temp_result_real := add_integer(c_in, d_in);
result_real <= temp_result_real;
else
result_real <= 0;
end if;
end process;
end behavioral;

## Slide 9
4.7,8,9 PACKAGE DECLARATIONS,BODIES,INSTANTIATION
Package declarations define the interface of a package, including constants, types, subprograms, and generics
Items declared in a package can be made visible in other design units through selection or use clauses
A package body must match its corresponding package declaration and follow it in the same declarative region
Package instantiation declarations create an instance of an uninstantiated package, associating actuals with generics through a generic map aspect
library IEEE;
use IEEE.std_logic_1164.all;
package mypackage is
constant default_value: integer := 10;
function double(value: integer) return integer;
function triple(value: integer) return integer;
end package mypackage;
package body mypackage is
function double(value: integer) return integer is
begin
return value * 2;
end function double;
function triple(value: integer) return integer is
begin
return value * 3;
end function triple;
end package body mypackage;
CODE EXAMPLE
entity packageexample is
port (
inputvalue : in integer;
outputvalue : out integer;
triplevalue : out integer
);
end packageexample;
architecture behavioral of packageexample is
use work.mypackage.all;
begin
process(inputvalue)
begin
outputvalue <= double(inputvalue);
triplevalue <= triple(inputvalue);
end process;
end behavioral;

## Slide 10
5. tYPES
5.1 General
5.2 Scalar Types
5.3 Composite Types
5.4 Access Types
5.5 File Types
5.6 Protected Types
5.7 String Representations
5.8 Unspecified Types
Chapter 5
Presenter:
Seyit Koçak

## Slide 11
A type is defined by a set of values and operations, including basic and predefined operations automatically provided
Composite types can be unconstrained, fully constrained, or partially constrained
Types are divided into five main categories: scalar, composite, access, file, and protected types
5.1 GENERAL
5.2 SCALAR TYPES
scalar_type_definition ::=
enumeration_type_definition
| integer_type_definition
| floating_type_definition
| physical_type_definition;
TYPE word_index IS RANGE 31 DOWNTO 0;
TYPE my_real IS RANGE 0.0 TO 9.99;
TYPE distance IS RANGE 0 TO 1E16
UNITS
-- Basiseinheit :
A -- Angström
-- Metrische Einheiten :
nm = 10 A; -- Nanometer
um = 1000 nm; -- Mikrometer
mm = 1000 um; -- Millimeter
cm = 10 mm; -- Centimeter
m = 1000 mm; -- Meter
km = 1000 m; -- Kilometer
END UNITS;

## Slide 12
CODE EXAMPLES
library IEEE;
use IEEE.std_logic_1164.all;
use IEEE.numeric_std.all;
entity bcdtoseven is
port (
sw : in std_logic_vector(13 downto 0);
clk : in std_logic;
seg : out std_logic_vector(6 downto 0);
an : out std_logic_vector(3 downto 0)
);
end bcdtoseven;
architecture behavioral of bcdtoseven is
type digit_type is (ones_digit, tens_digit, hundreds_digit, thousands_digit);
signal current_digit : digit_type := ones_digit;
signal ones, tens, hundreds, thousands : std_logic_vector(3 downto 0);
signal slow_clk : std_logic := '0';
signal clk_divider : integer := 0;
type binary_value_type is (
ZERO, ONE, TWO, THREE, FOUR, FIVE,
SIX, SEVEN, EIGHT, NINE );
function binary_to_seven_segment(input : std_logic_vector(3 downto 0)) return std_logic_vector is
variable seg_output : std_logic_vector(6 downto 0);
begin
case input is
when ZERO => seg_output := "1000000";
when ONE => seg_output := "1111001";
when TWO => seg_output := "0100100";
when THREE => seg_output := "0110000";
when FOUR => seg_output := "0011001";
when FIVE => seg_output := "0010010";
when SIX => seg_output := "0000010";
when SEVEN => seg_output := "1111000";
when EIGHT => seg_output := "0000000";
when NINE => seg_output := "0010000";
when others => seg_output := "1111111";
end case;
return seg_output;
end function;
begin
process(clk)
begin
if rising_edge(clk) then
if clk_divider = 50000 then
slow_clk <= not slow_clk;
clk_divider <= 0;
else
clk_divider <= clk_divider + 1;
end if;
end if;
end process;
process(sw)
variable value_int : integer;
begin
value_int := to_integer(unsigned(sw));
thousands <= std_logic_vector(to_unsigned(value_int / 1000, 4));
hundreds <= std_logic_vector(to_unsigned((value_int / 100) mod 10, 4));
tens <= std_logic_vector(to_unsigned((value_int / 10) mod 10, 4));
ones <= std_logic_vector(to_unsigned(value_int mod 10, 4));
end process;
process(current_digit, ones, tens, hundreds, thousands)
begin
case current_digit is
when ones_digit => an <= "1110"; seg <= binary_to_seven_segment(ones);
when tens_digit => an <= "1101"; seg <= binary_to_seven_segment(tens);
when hundreds_digit => an <= "1011"; seg <= binary_to_seven_segment(hundreds);
when thousands_digit => an <= "0111"; seg <= binary_to_seven_segment(thousands);
when others => an <= "1111"; seg <= (others => '1');
end case;
end process;
process(slow_clk)
begin
if rising_edge(slow_clk) then
case current_digit is
when ones_digit => current_digit <= tens_digit;
when tens_digit => current_digit <= hundreds_digit;
when hundreds_digit => current_digit <= thousands_digit;
when thousands_digit => current_digit <= ones_digit;
when others => current_digit <= ones_digit;
end case;
end if;
end process;
end behavioral;

## Slide 13
VHDL arrays store multiple elements of the same type in an organized way and provide fast access
Arrays are used for grouping data, modeling multidimensional structures, and performing operations on large data sets
They serve as a foundation for creating dynamic data structures and algorithms, enabling efficient data management and simulation
Record types in VHDL allow grouping of different types of elements under a single name, where each element can have a different data type
Record types are useful for modeling complex data structures where multiple related values need to be stored together, such as a set of properties for an object
5.3 COMPOSITE TYPES
composite_type_definition ::=
array_type_definition |
record_type_definition

## Slide 14
Access type provides a way to point to objects
Access type allows dynamically creating objects in memory
The DEALLOCATE procedure releases allocated memory
5.4 ACCSESS TYPES
5.5 FILE TYPES
In VHDL, file types are used to define objects that represent files in the system, and the data within the file is constrained by a specific subtype
A file can be managed with operations like READ, WRITE, SEEK, and FLUSH, where the reading and writing modes determine the type of operation
type Int_Ptr is access Integer;
variable Ptr : Int_Ptr := null; -- Initially points to nothing
-------------------------------------------------------------------------
Ptr := new Integer(5); -- Creates an integer object in memory with a value of 5
-------------------------------------------------------------------------
DEALLOCATE(Ptr); -- Frees the memory and sets Ptr to null

## Slide 15
When to Use Protected Types?
When concurrent data access occurs (multiple processes need to access the same data simultaneously)
When the secure management of shared resources is required
When control and organization are necessary for data manipulation
When restricted access to critical sections is needed to ensure consistency and avoid race conditions
5.6 PROTECTED TYPES
library IEEE;
use IEEE.std_logic_1164.all;
use IEEE.numeric_std.all;
protected type sharedcounter is
procedure increment;
function getvalue return integer;
end protected;
protected body sharedcounter is
variable count: integer := 0;
procedure increment is
begin
count := count + 1;
end procedure;
function getvalue return integer is
begin
return count;
end function;
end protected body;
library IEEE;
use IEEE.std_logic_1164.all;
use IEEE.numeric_std.all;
use work.sharedcounter.all;
entity protectedtypes is
port (
clk : in std_logic;
out_counter : out integer
);
end protectedtypes;
architecture behavior of protectedtypes is
shared variable counter: sharedcounter;
begin
process(clk)
begin
if rising_edge(clk) then
counter.increment;
end if;
end process;
process(clk)
begin
if rising_edge(clk) then
out_counter <= counter.getvalue;
end if;
end process;
end behavior;
CODE EXAMPLES

## Slide 16
Why is String Representations under the types section?
Strings are a VHDL type: Defined as arrays of characters, part of the type hierarchy
Ensures type safety: Fixed or constrained strings prevent design errors
Essential for testing: Key for assertions, debugging, and messages
5.7 STRING REPRESENTATIONS
5.8 UNSPECIFIED TYPES
Unspecified types allow abstract type definitions in VHDL
They are used for generics, ports, and parameters
Types are determined during elaboration
They support scalar, array, access, and file types
These types enable flexible and reusable designs

## Slide 17
6.1 General
6.2 Type Declarations
6.3 Subtype Declarations
6.4 Objects
6.5 Interface Declarations
6.6 Alias Declarations
6.7 Attribute Declarations
6.8 Component Declarations
6.9 Group Template Declarations
6.10 Group Declarations
6.11 PSL Clock Declarations
6. DECLARATIONS
Chapter 6
Presenter:
Mert Ecevit

## Slide 18
Custom structures and types for more accurate data representation are made possible by type declarations, which establish new data types in VHDL
6.2 Type Declarations
6.3 Subtype Declarations
A type together with a constraint
6.4 Objects
In VHDL, an object is a container for a value of a given type
6.5 Interface Declarations
• Interface declarations define interface objects of a precisely defined type
• Interface objects are interface constants, interface signals, interface variables and interface files
6.6 Alias Declarations
An alias is an alternative name for an existing object (signal, variable or constant)
They don’t define a new object

## Slide 19
Attributes are user-defined properties attached to types, signals, entities, etc.
They can store metadata or control simulation aspects
6.7 Attribute Declarations
6.8 Component Declarations
Components act as templates for modules or logic blocks that can be instantiated multiple times in a design which allows reusability and modular design
6.11 PSL Clock Declarations
A group template declaration declares a group template, which defines the allowable classes of named entities that can appear in a group
6.9 Group Template Declarations
• A group declaration declares a group, a named collection of named entities
6.10 Group Declarations
When doing formal verification, module’s properties have to expresses using the Property Specification Language (PSL)

## Slide 20
Code Example
library IEEE;
use IEEE.std_logic_1164.all;
--type and subtype declarations package custom is
type boolean is (false, true);
type bit_vector is array (7 downto 0) of bit; --type declarations subtype my_vector is std_logic_vector (3 downto 0);
subtype word is unsigned(15 downto 0); --subtype declarations
end package custom;
sum <= '1';
carry1 <= bit(carry);
carry2 <= '1';
result <= temp_result;
end if;
end process;
end bhv;
entity example is
port (
clk : in std_logic;
reset : in std_logic;
result : out std_logic
);
end example;
architecture bhv of example is
-- Constant declaration
constant loop_number : integer := 7;
-- Signal declarations
signal sum, carry1, carry2 : bit := '0';
-- Variable declaration (used in a process)
signal carry : std_logic := '0';
begin
process(clk, reset)
variable temp_result : std_logic := '0';
begin
if reset = '1' then
sum <= '0';
carry1 <= '0';
carry2 <= '0';
carry <= '0';
temp_result := '0';
result <= '0';
elsif rising_edge(clk) then
for i in 0 to loop_number loop
if i mod 2 = 0 then
carry <= '1';
temp_result := carry;
else
carry <= '0';
temp_result := carry;
end if;
end loop;

## Slide 21
Code Examples
--Interface Declaration
type axi4_lite_write_address_type is record
aw_addr : std_logic_vector ;
aw_prot : std_logic_vector ;
aw_valid : std_logic ;
aw_ready : std_logic ;
end record axi4_lite_write_address_type ;
--encapsulation
view axi4_lite_write_address_master_view of axi4_lite_write_address_type is
aw_addr : out ;
aw_prot : out ;
aw_valid : out ;
aw_ready : in ;
end view axi4_lite_write_address_master_view of ;
-- a view declaration for the mode replacement
axi_master1 : view axi4_lite_master_view ;
axi_master2 : view axi4_lite_master_view of axi4_lite_type ;
axi_responder1 : view axi4_lite_responder_view ;
axi_responder2 : view axi4_lite_responder_view ;
--Use the interface in an entity declaration
library IEEE;
use IEEE.STD_LOGIC_1164.ALL;
entity timing_example is
port (
clk : in std_logic;
reset : in std_logic;
signal_in : in std_logic;
signal_out : out std_logic
);
end timing_example;
architecture behavioral of timing_example is
-- Constant declaration
constant tc : time := 2.5 ns;
-- Alias declaration
alias delay : time is tc;
begin
process(clk, reset)
begin
if reset = '1' then
signal_out <= '0' after delay;
elsif rising_edge(clk) then
signal_out <= signal_in after delay;
end if;
end process;
end behavioral;

## Slide 22
Code Examples
--Component Declaration
library IEEE;
use IEEE.std_logic_1164.all;
entity component_instantiation is
port (add1, add2: in integer;
sum_1: out integer);
end;
architecture example of component_instantiation is
component adder is
port (a, b: in integer;
sum: out integer);
end component;
begin
component_inst: adder_component
port map (a => add1
b => add2,
sum => sum);
end example;
--Group Declaration
architecture rtl of Ent is
group operations is (signal <>);
group adders: operations (x, y, z);
begin
a1: x <= a + b;
a2: y <= c + d;
a3: z <= e + f;
end architecture rtl;
--Attribute Declaration
library IEEE;
use IEEE.std_logic_1164.all;
package my_types is
type t is (a, b, c, d, e);
subtype s is t range d downto b;
end package my_types;
entity attribute_example is
port (
input_a : in std_logic_vector(7 downto 0);
input_b : in std_logic_vector(7 downto 0);
result : out std_logic_vector(15 downto 0)
);
end attribute_example;
architecture behavioral of Attribute_Example is
use work.my_types.all;
signal signal_a : std_logic_vector(7 downto 0);
signal signal_b : std_logic_vector(7 downto 0);
signal product : std_logic_vector(15 downto 0);
signal my_enum : s := d;
begin
process
begin
signal_a <= input_a;
signal_a <= input_b;
product <= std_logic_vector(unsigned(signal_a) * unsigned(signal_b));
product(product'left) <= '1';
wait;
end process;
end behavioral;

## Slide 23
7.1 General
7.2 Attribute specification
7.3 Configuration specification
7.4 Disconnection specification
7. Specifications
Chapter 7
Presenter:
Furkan Kaya

## Slide 24
7.1 GENERAL
Specifications in VHDL, which define additional properties or configurations for design elements, increasing clarity, control, and customization in hardware modeling.
Associate attributes with VHDL objects to define additional properties or behaviors.
attribute pin_no of cin: signal is 10;
attribute pin_no of cout: signal is 5;
attribute location of adder1: label is (10,15);
attribute location of others: label is (25,77);
attribute capaticance of all: signal is 15 pf;
attribute implementation of g1: group is "74ls152";
attribute rising_delay of c2q: group is 7.2 ns;
Define how components are bound to specific entities or architectures within a design.
use work.global_signals.all;
configuration different of half_adder is
for structure
for l1: xor_gate
generic map (2.9 ns, 3.6 ns);
end for;
for l2: and_gate
generic map (2.8 ns, 3.25 ns)
port map (i2 => tied_high);
end for;
end for;
end configuration different;
Define conditions under which resolved signals can be disconnected during simulation.
disconnect s: t after 10 ns;
disconnect others: t after 5 ms;
disconnect all: t after 273 us;
10 ns, 5 ms and 273 us are
just arbitrary time expressions.
EX-1
EX-3
EX-2
7.2 ATTRIBUTE
SPECIFICATION
7.3 CONFIGURATION
SPECIFICATION
7.4 DISCONNECTION
SPECIFICATION
All of the examples are taken from "IEEE1076-2019" document

## Slide 25
8. NAMES
8.1 General
8.2 Simple Names
8.3 Selected Names
8.4 Indexed Names
8.5 Slice Names
8.6 Attribute Names
8.7 External Names
Chapter 8
Presenter:
Orhan Çalışkan

## Slide 26
Names can include :
  Simple Name (represents a single entity)
  Operator Symbol (represent operators)
  Character Literal (represent a single character) (not in VHDL2002)
  Selected Name (provide access to an element from a package or record)
  Indexed Name (access to a specific element of an array or vector)
  Slice Name (represent a specific range of an array or vector)
  Attribute Name (represent an Attribute)
  External Name (represent an external entity) (not in VHDL2002)
8.1 GENERAL
8.2 SIMPLE NAMES
Simple names is the name you directly give to an object (signal, variable, entity, architecture, function, procedure, package etc.)

## Slide 27
Selected names access an object from within another object or from a library
  Provide modularity and readability
  Include prefix and suffix
  Selected_name ::= prefix.suffix
  IEEE.std_logic_1164.all
8.3 SELECTED NAMES
8.4 INDEXED NAMES
Indexed names used in VHDL to access specific elements of arrays
  One index for each dimension
  Indexes must be within the bounds of the array
  indexed_name ::= prefix ( expression { , expression } )

## Slide 28
Slice name represents a segment of consecutive elements from an array
  Follows the format prefix(discrete_range)
  data(15 downto 0) -- A slice with a descending range
  data(0 to 15) -- A slice with a ascending range
  data(0 downto 15) -- A null slice
8.5 SLICE NAMES
8.6 ATTRIBUTE NAMES
Attribute name represents a value, function, type, range, signal, or constant associated with an entity
  follows the format : prefix [signature] 'attribute_designator [ (expression) ]
  clk'delayed(5 ns) -- clk signal delayed by 5 ns

## Slide 29
External name denotes an object declared in the design hierarchy containing the external name
  External Variable Name: Provides access to variables defined in other regions
  External Signal Name: Provides access to signals defined in other regions
  External Constant Name: Allows access to constants from external regions
  Package Pathname: Provides access to a specific element within a package. It is used to access elements defined within a specific package in the design
  Absolute Pathname: Starts from the root of the design and encompasses the entire hierarchy. It provides access to elements at the highest level of the design
  Relative Pathname: Accesses an element by moving up or down from the current location. It provides dynamic access based on the current position
  Partial Pathname: Refers to a specific element in more detail. It points to a particular part of the design
8.7 EXTERNAL NAMES

## Slide 30
  library IEEE;
  use IEEE.std_logic_1164.all; --This line is example for selected name
  use work.example_package.all; --This line is example for external name
  Entity my_design is --my_design is a simple name
  port
  (
  clk : in std_logic;
  rst : in std_logic;
  input_vld : in std_logic;
  comm_input : in std_logic_vector (15 downto 0); --comm_input port is a slice name
  output_vld : in std_logic;
  data_out : out std_logic_vector(15 downto 0) --data_out port is a slice name
  );
  end my_design;
  architecture behavioral of my_design is
  signal data : std_logic_vector(data_upper_lmt downto data_lower_lmt); --data is a static name
  begin
CODE EXAMPLE
  process(clk) begin
  if (clk'event and clk = '1') then --clk'event is a attribute name
  if(input_vld = '1') then
  data <= comm_input(15 downto 1) & not comm_input(0);
  --comm_input(0) is a indexed name
  end if;
  if(output_vld = '1') then
  data_out <= data;
  end if;
  end if;
  end process;

## Slide 31
9.1 General
9.2 Operators
9.3 Operands
9.4 Static Expressions
9.5 Universal Expressions
9. EXPRESSIONS
Chapter 9
Presenter:
Mert Ecevit

## Slide 32
A formula that defines the computation of a value
9.2 Operators

## Slide 33
The operands in an expression includes literals, aggregates, function, calls, type conversions
9.3 Operands
9.4 Static Expressions
9.5 Universal Expressions
• Utilized in constant declarations or restrictions; fully computed at compile time
• There are two categories of static expression: – If every operator in expression is an implicit defined operator, these are called locally static expressions – If every in the expression is a pure function and every primary in the expression is a global static primary, they are called globally static expressions
• A universal expression is either an expression that delivers a result of type universal integer or one that delivers a result of type universal real
• The same operations are predefined for the type universal integer as for any integer type, type universal real as for any floating-point type
• In addition, these operations include the multiplication and division operators

## Slide 34
10.1 General
10.2 Wait Statement
10.3 Assertion Statement
10.4 Report Statement
10.5 Signal Assignment Statement
10.6 Variable Assignment Statement
10.7 Procedure Call Statement
10.8 If Statement
10.9 Case Statement
10.10 Loop Statement
10.11 Next Statement
10.12 Exit Statement
10.13 Return Statement
10.14 Null Statement
10.15 Sequential Block Statement
10. SEQUENTIAL STATEMENTS
Chapter 10
Presenter:
Yunus Küçük

## Slide 35: 10.1 General
Sequential statements are used to define algorithms for the execution of a subprogram or process; they execute in the order in which they appear

## Slide 36: 10.2 WaIt Statement
There are 4 different types of wait statements which are:
  wait: it will suspend code forever
  wait on: is equivalent to using a sensitivity list in a process. As soon as any of the signals in the wait on list changes, the code will continue to execute
  wait until: it will suspend a process until the condition of the wait is true
  wait for: is never synthesizable. However, it is still very useful for test benches and for bus functional models. Wait for must be followed by some amount of time, for example 10 ns
  One additional note: A process that has a sensitivity list can not contain any wait statements

## Slide 37: 10.3 Assertıon statement
Checks that a specified condition is true and reports an error if it is not
Syntax:
[ label: ] assert condition [ report string_expression ] [ severity expression ];
Description:
The assertion statement has three optional fields and usually all three are used
The condition specified in an assertion statement must evaluate to a Boolean value (true or false). If it is false, it is said that an assertion violation occurred
The expression specified in the report clause must be of predefined type String and is a message to be reported when assertion violation occurred
If the severity clause is present, it must specify an expression of predefined type Severity_Level, which determines the severity level of the assertion violation
The Severity_Level type is specified in the Standard package and contains the following values: Note, Warning, Error, and Failure
If the severity clause is omitted it is implicitly assumed to be Error.
assert not (Reset = '0' and Set = '0') report "set-reset conflict" severity Failure;
assert result = ExpectedResults report "results differ from expected results" severity Warning;
Notes:
The message is displayed when the condition is false, therefore the message should be an opposite to the condition
The concurrent assertion statement is a passive process and as such can be specified in an entity
The concurrent assertion statement monitors the specified condition continuously.
Synthesis tools generally ignore assertion statements
CODE EXAMPLE

## Slide 38: 10.4 report statement
A statement that displays a message
Syntax:
[ label: ] report string_expression [ severity expression ];
Description:
The main difference between the report statement and the assertion statement is that the message in the report statement is displayed unconditionally
If the severity clause is present, it must specify an expression of predefined type Severity_Level, which has the values: Note, Warning, Error, and Failure
report "End of simulation" severity note;
Notes:
If the severity clause is omitted in a report statement it is implicitly assumed to be Note
If the severity clause is used then the default is Error
CODE EXAMPLE

## Slide 39: CODE EXAMPLE of waıt statements
entity T07_WaitOnUntilTb is
end entity;
architecture sim of T07_WaitOnUntilTb is
signal CountUp : integer := 0;
signal CountDown : integer := 10;
begin
process is
begin
CountUp <= CountUp + 1;
CountDown <= CountDown - 1;
wait for 10 ns;
end process;
process is
begin
wait on CountUp, CountDown;
report "CountUp=" & integer'image(CountUp) &
" CountDown=" & integer'image(CountDown);
end process;
process is
begin
wait until CountUp = CountDown;
report "Jackpot!";
end process;
end architecture;

## Slide 40
Note: CountUp=1 CountDown=9
Time: 0 ps Iteration: 1 Process: /T07_WaitOnUntilTb/line__20 File: D:/Projects/Deneme1/Deneme1.srcs/sources_1/new/deneme.vhd
Note: CountUp=2 CountDown=8
Time: 10 ns Iteration: 1 Process: /T07_WaitOnUntilTb/line__20 File: D:/Projects/Deneme1/Deneme1.srcs/sources_1/new/deneme.vhd
Note: CountUp=3 CountDown=7
Time: 20 ns Iteration: 1 Process: /T07_WaitOnUntilTb/line__20 File: D:/Projects/Deneme1/Deneme1.srcs/sources_1/new/deneme.vhd
Note: CountUp=4 CountDown=6
Time: 30 ns Iteration: 1 Process: /T07_WaitOnUntilTb/line__20 File: D:/Projects/Deneme1/Deneme1.srcs/sources_1/new/deneme.vhd
Note: CountUp=5 CountDown=5
Time: 40 ns Iteration: 1 Process: /T07_WaitOnUntilTb/line__20 File: D:/Projects/Deneme1/Deneme1.srcs/sources_1/new/deneme.vhd
Note: Jackpot!
Time: 40 ns Iteration: 1 Process: /T07_WaitOnUntilTb/line__29 File: D:/Projects/Deneme1/Deneme1.srcs/sources_1/new/deneme.vhd
Note: CountUp=6 CountDown=4
Time: 50 ns Iteration: 1 Process: /T07_WaitOnUntilTb/line__20 File: D:/Projects/Deneme1/Deneme1.srcs/sources_1/new/deneme.vhd

## Slide 41: 10.5 SIGNAL ASSIGNMENT statement
Description:
Modifies the projected output waveforms contained in the drivers of one or more signals
Schedules a force for one or more signals or schedules release of one or more signals
Syntax:
signal_assignment_statement ::=
[ label : ] simple_signal_assignment |
[ label : ] conditional_signal_assignment |
[ label : ] selected_signal_assignment
CODE EXAMPLE
-- Assignments using inertial delay:
-- The following three assignments are equivalent to each other:
Output_pin <= Input_pin after 10 ns;
Output_pin <= inertial Input_pin after 10 ns;
Output_pin <= reject 10 ns inertial Input_pin after 10 ns;
-- Assignments with a pulse rejection limit less than the time
-- expression:
Output_pin <= reject 5 ns inertial Input_pin after 10 ns;
Output_pin <= reject 5 ns inertial Input_pin after 10 ns,
not Input_pin after 20 ns;
--Conditional signal assignment
target <= delay_mechanism
waveform1 when condition1 else
waveform2 when condition2 else
···
···
waveformN-1 when conditionN-1 else
waveformN when conditionN

## Slide 42: 10.6 varıable ASSIGNMENT statement
Description:
The purpose of variables in VHDL is in cases where you need to drive outputs of a process by something that will change throughout the process, and you need to capture each of those changes
Notes:
Variables can only be used inside processes
Any variable that is created in one process cannot be used in another process
Variables need to be defined after the keyword process but before the keyword begin
Variables are assigned using the := assignment symbol
Variables that are assigned immediately take the value of the assignment
The most important thing to understand is that variables immediately take the value of their assignment

## Slide 43
library ieee;
use ieee.std_logic_1164.all;
use ieee.numeric_std.all;
entity Variable_Statement is
end entity;
architecture sim of Variable_Statement is
signal MySignal : integer := 0;
begin
process
variable MyVariable : integer := 0;
begin
MyVariable := MyVariable + 1;
MySignal <= MySignal + 1;
report "MyVariable=" & integer'image(MyVariable) &
", MySignal=" & integer'image(MySignal);
wait for 10ns;
end process;
end architecture;
Note: MyVariable=1, MySignal=0
Note: MyVariable=2, MySignal=1
Note: MyVariable=3, MySignal=2
Note: MyVariable=4, MySignal=3
Note: MyVariable=5, MySignal=4
Note: MyVariable=6, MySignal=5
Note: MyVariable=7, MySignal=6
Note: MyVariable=8, MySignal=7
Note: MyVariable=9, MySignal=8
.
.
.
CODE EXAMPLE

## Slide 44: 10.7 procedure CALL statement
Description:
A procedure is a type of subprogram in VHDL which can help us avoid repeating code
  Sometimes the need arises to perform identical operations several places throughout the design
  While creating a module might be overkill for minor operations, a procedure is often what you want
Procedures can be declared within any declarative region
  The scope of the procedure will be limited to wherever it’s declared, architecture, package, or process
  Whenever you call the procedure, it will behave like the code of the procedure was inserted where it was called from
A procedure’s parameter list defines its inputs and outputs, kind of like a mini-module
  It can be a signal or a constant, but unlike a module, it can also be a variable
  You can declare objects between the “is” and “begin” keywords that are only valid inside the procedure
  These may include constants, variables, types, subtypes, and aliases, but not signals
Syntax:
procedure <procedure_name>
(signal|variable|constant <name1> : in|out|inout <type>;
signal|variable|constant <name2> : in|out|inout <type>;
... ) is
<declarations_for_use_within_the_procedure>
begin
<code_performed_by_the_procedure_here>
end procedure;

## Slide 45: 10.8 ıf statement
Description:
Selects for execution one or none of the enclosed sequences of statements, depending on the value of one or more corresponding conditions
Syntax:
if_label : if condition then
sequence_of_statements
elsif condition then
sequence_of_statements
else
sequence_of_statements
end if;

## Slide 46
entity If_Statement is
end entity;
architecture sim of If_Statement is
signal CountUp : integer := 0;
signal CountDown : integer := 10;
begin
process is
begin
CountUp <= CountUp + 1;
CountDown <= CountDown - 1;
wait for 10 ns;
end process;
process is
begin
if CountUp > CountDown then
report "CountUp is larger";
elsif CountUp < CountDown then
report "CountDown is larger";
else
report "They are equal";
end if;
wait on CountUp, CountDown;
end process;
end architecture;
Note: CountDown is larger
Time: 0 ps Iteration: 0
Note: CountDown is larger
Time: 0 ps Iteration: 1
Note: CountDown is larger
Time: 10 ns Iteration: 1
Note: CountDown is larger
Time: 20 ns Iteration: 1
Note: CountDown is larger
Time: 30 ns Iteration: 1
Note: They are equal
Time: 40 ns Iteration: 1
Note: CountUp is larger
Time: 50 ns Iteration: 1
Note: CountUp is larger
Time: 60 ns Iteration: 1
Note: CountUp is larger
Time: 70 ns Iteration: 1
Note: CountUp is larger
Time: 80 ns Iteration: 1
Note: CountUp is larger
Time: 90 ns Iteration: 1
Note: CountUp is larger
Time: 100 ns Iteration: 1
Note: CountUp is larger
CODE EXAMPLE

## Slide 47: 10.9 case statement
Syntax:
case <expression> is
when <choice> =>
code for this branch
when <choice> =>
code for this branch
...
end case;
Description:
Works exactly the way that a switch statement in C works
  Given an input, the statement looks at each possible condition to find one that the input signal satisfies
  Useful to check one input signal against many combinations
Just like in C, the VHDL designer should always specify a default condition provided that none of the case statements are chosen
  This is done via the “when others =>” statement (check the code example in the next page)

## Slide 48: 10.10 loop statement
Syntax:
for <name> in <lower_limit> to <upper_limit> loop
<statement>;
<statement>;
end loop;
while <condition> loop
<statement>;
<statement>;
end loop;

## Slide 49
library IEEE;
use IEEE.std_logic_1164.all;
use IEEE.numeric_std.all;
entity loop_Statement is
end entity;
architecture sim of loop_statement is
begin
for_process : process is
begin
for i in 1 to 10 loop
report "i = " & integer'image(i);
end loop;
wait;
end process;
while_process : process is
variable j : integer := 0;
begin
while j < 10 loop
report "j = " & integer'image(j);
j := j + 2;
end loop;
wait;
end process;
end architecture;
CODE EXAMPLE

## Slide 50: 10.11 next statement
Completes execution of one of the iterations of an enclosing loop statement, making it jump back to the top of that loop
  The completion is conditional if the statement includes a condition
Syntax:
[ label: ] next [ loop_label ] [ when condition ];
Description:
The next statement allows to skip a part of an iteration loop
  If the condition specified after the when reserved word is true, or if there is no condition at all, then the statement is executed
  This results in skipping all statements below it until the end of the loop and passing the control to the first statement in the next iteration
A next statement may specify the name of the loop it is expected to influence. If no label is supported then the statement applies to the innermost enclosing loop.
Note:
Often confused with the exit statement
  The difference is that the exit statement "exits" the loop entirely, while the next statement skips to the "next" loop iteration
L1: loop
k:= 0;
L2: for CountValue in 1 to 8 loop
next when CountValue = N; -- jump to next itteration of loop L2
if A(k):= 'U' then
next L1; -- jump to top of loop L1
end if;
k:= k + 1;
end loop L2;
end loop L1;
CODE EXAMPLE

## Slide 51: 10.12 Exıt statement
Finishes or exits the execution of an enclosing loop statement
Syntax:
[ label: ] exit [ loop_label ] [ when condition ];
Description:
Terminates entirely the execution of the loop in which it is located
If a condition is placed on the exit statement, then the execution of the exit statement depends on the condition placed at the end of the statement
When the condition is true (or if there is no condition at all) the exit statement is executed, and the control is passed to the first statement after the end loop
  L1: loop
  L2: for I in 0 to 7 loop
  if B(I) = 'U' then
  exit L1;
  end if;
  exit when I = M;
  end loop L2;
  ...
  end loop L1;
Note: The exit statement is often confused with the next statement, the difference between the two is that the exit statement "exits" the loop entirely, while the next statement skips to the "next" loop iteration (in other words, "exits" only the current iteration of the loop)
CODE EXAMPLE

## Slide 52: 10.13 Return statement
Completes the execution of the innermost enclosing function or procedure body
Syntax:
[ label: ] return [ expression ];
Description :
Ends the execution of a subprogram (procedure or function) in which it appears
Causes an unconditional jump to the end of the subprogram
Only allowed in a procedure or function body
In a procedure it may not return any value, while a return in a function must return a value consistent with the return type of the function
return X + Y;
CODE EXAMPLE

## Slide 53: 10.14 null statement
A null statement performs no action
Syntax:
[ label : ] null ;
Description:
The execution of the null statement has no effect other than to pass on to the next statement

## Slide 54: 10.15 SEQUENTIAL BLOCK statement
Encloses a sequence of sequential statements
Could be nested
Syntax:
sequential_block_statement ::=
[ sequential_block_label : ] block [ is ]
sequential_block_declarative_part
begin
sequential_block_statement_part
end [ block ] [ sequential_block_label ] ;
sequential_block_declarative_part ::=
{ process_declarative_item }
sequential_block_statement_part ::=
{ sequential_statement }
Description:
The execution of a sequential block statement consists of the elaboration of the sequential block declarative part followed by the execution of the statements in the sequential block statement part
If a label appears at the end of a sequential block statement, it shall repeat the sequential block label
It is an error if a variable declaration in a process declarative part declares a shared variable

## Slide 55
11.1 General
11.2 Block Statement
11.3 Process Statement
11.4 Concurrent Procedure Call Statements
11.5 Concurrent Assertion Statements
11.6 Concurrent Signal Assignment Statements
11.7 Component Instantiation Statements
11.8 Generate Statements
11. Concurrent statements
Chapter 11
Presenter:
Mert Ecevit

## Slide 56
A block statement defines an internal block representing a portion of a design
11.2 Block Statement
11.3 Process Statement
Processes the signals associated with architecture
11.4 Concurrent Procedure Call Statements
Procedures can also be used like a concurrent statement, when it is called from a concurrent code region
11.5 Concurrent Assertion Statements
A concurrent assertion statement represents a passive process statement containing the specified assertion statement

## Slide 57
11.6 Concurrent Assertion Statements
A concurrent assertion statement represents a passive process statement containing the specified assertion statement.
11.7 Component Instantiation Statements
Component instantiation allows you to instantiate one design unit (component) inside another design unit to create a hierarchically structured design description.
11.8 Generate Statements
Generate statements are used to accomplish one of two goals:
– Replicating Logic in VHDL
– Turning on/off blocks of logic in VHDL

## Slide 58
-Block Statement
architecture rtl of dsp is
...
begin
mac_unit: block
port (a, b: in float32; mac_out: out float32);
port map (a = > x, b = > y, mac_out = > acc);
signal multiplier_out: float32;
signal adder_out: float32 ;
begin
multiplier_out <= a * b;
adder_out <= multiplier_out + mac_out;
process (clock, reset) begin
if reset then
mac_out <= ( others = > '0');
elsif rising_edge(clock) then
mac_out <= adder_out;
end if ;
end process ;
end block ;
...
end architecture rtl;
--Process statement
library IEEE;
use IEEE.std_logic_1164.all;
use IEEE.numeric_std.all;
entity D_FF is
port( d,clk: in std_logic;
q: out std_logic);
end D_FF;
architecture bhv of D_FF is
begin
process(clk)
begin
if rising_edge(clk) then
Q <= D;
end if;
end process;
end bhv;
--Concurrent Signal Assignment
library IEEE;
use IEEE.IEEE.std_logic_1164.all;
entity add_1 is
port ( a, b, cin: in bit;
s, cout: out bit);
end add_1;
architecture concurrent of add_1 is
signal s1, s2, s3, s4: bit;
begin
s1 <= b xor cin;
s2 <= a and b;
s3 <= a and cin;
s4 <= b and cin;
s <= a xor s1;
cout <= s2 or s3 or s4;
end concurrent;
CODE EXAMPLES

## Slide 59
--Concurrent Procedure Call Statement
library IEEE;
use IEEE.std_logic_1164.all;
use IEEE.numeric_std.all;
entity adder is
port (a, b: in integer;
sum: out integer);
end adder;
architecture bhv of adder is
procedure add(a, b: in integer;
signal sum: out integer) is begin
sum <= a + b;
end;
…
begin
adder_procedure : add(add1, add2, sum2),
end architecture bhv;
--equivalent statements
architecture sensitiviy_list of adder is
begin
process(add1, add2)
begin
add(add1, add2, sum2);
end process;
end architecture; --sensitivity list
architecture wait_statement of adder is
begin
process
begin
add(add1, add2, sum2);
wait on add1, add2;
end process;
end wait_statement; --wait statement
--Concurrent Assertion Statement
library IEEE;
use IEEE.IEEE.std_logic_1164.all;
use IEEE._std_logic_arith.all;
use IEEE.std_logic_unsigned.all;
entity tb_address_check is
end tb_address_check;
architecture behavior of tb_address_check is
signal address : STD_LOGIC_VECTOR(31 downto 0);
component address_check
port ( address : in STD_LOGIC_VECTOR(31 downto 0));
end component;
begin
uut: address_check Port map (address => address);
stim_proc: process
begin
address <= x"0000_1234"; wait for 10 ns;
address <= x"9000_1234"; wait for 10 ns;
address <= x"4000_0000"; wait for 10 ns;
address <= x"1000_0000"; wait for 10 ns;
wait;
end process;
-- Concurrent assertion
assert (to_integer(unsigned(address)) < x"1000_0000" or to_integer(unsigned(address)) >= x"8000_0000")
report "Invalid access at address " & to_string(address)
severity warning;
end behavior;
CODE EXAMPLES

## Slide 60
--Component Instantiation
library IEEE;
use IEEE.std_logic_1164.all;
entity component_instantiation is
port (add1, add2: in integer;
sum_1: out integer);
end;
architecture example of component_instantiation is
component adder is
port (a, b: in integer;
sum: out integer);
end component;
begin
component_inst: adder_component
port map (a => add1
b => add2,
sum => sum);
end example;
--Entity Instantiation and Generate Statement
entity full_adder1 is
Port (a : in std_logic;
b : in std_logic;
carry_in : in std_logic;
sum : out std_logic;
carry_out: out std_logic);
end full_adder1;
--full code
library IEEE;
use IEEE.IEEE.std_logic_1164.all;
use IEEE._std_logic_arith.all;
use IEEE.std_logic_unsigned.all;
architecture structural of adder is
signal carry_in_vector: std_logic_vector( 0 to WIDTH- 1);
signal carry_out_vector: std_logic_vector( 0 to WIDTH- 1);
begin
instantiate_adders: for i in 0 to WIDTH- 1 generate --generate statement and entity instantiation
adder_bit: entity work.full_adder1
port map (a = > a(i), b = > b(i), carry_in = > carry_in_vector(i),
sum = > sum(i), carry_out = > carry_out_vector(i));
end generate ;
carry_in_vector <= (carry_in, carry_out_vector( 0 to WIDTH- 2));
carry_out <= carry_out_vector(WIDTH- 1);
end structural;
CODE EXAMPLES

## Slide 61
12. Scope and vısıbılıty
12.1 Declerative Region
12.2 Scope of Decleration
12.3 Visibility
12.4 Use Clauses
12.5 The Context of Overload Resolution
Chapter 12
Presenter:
Orhan Çalışkan

## Slide 62
  Declarative region in VHDL is a text area where declarations and definitions are valid
    Entity and its associated architecture body
    Subprograms (procedures/functions) and their bodies
    Packages and their bodies (if any)
    Process, block, loop, and generate statement
  Declarations belong to the innermost region where they are defined
  Structures like the architecture body are not affected by the scope outside their own region
  Root Declarative Region: The top-level region of each design
  Library Declarative Region: Defined for each design library, encompassing all units within the library
12.1 DECLERATIVE REGION
    library ieee;
    use ieee.std_logic_1164.all;
    entity myentity is
    -- entity declarative region
    ...
    end myentity;
    architecture behavioral of myentity is
    -- architecture declarative region
    begin
    process(...)
    -- process declarative region
    begin
    end process;
    end behavioral;

## Slide 63
  The portion of code where a declaration or named entity is valid
  Scope defines the usage area of the declaration or entity
  Scope starts from the declaration and extends to the end of the innermost declarative region
  The scope of an architecture body is limited to its internal region
  Structures like package, record type, subprogram parameters, generics and ports extend their scope to the enclosing unit
  Architecture body is included in the scope of its associated Entity
  Block configurations and Library declarations can extend the scope
  PSL verification units can be linked to extend the scope into verification structures.
12.2 SCOPE OF DECLERATIONS

## Slide 64
  Visibility determines the area where elements of a declaration are valid. A declaration can only be used within its visible scope
  Multiple declarations with the same name can be made, and the visibility rules determine which declaration is valid
  Component configuration and block configuration declarations can become visible by selection
  Use clauses modify the visibility of declarations. Hiding conceals the same-named declarations from the outer scope
  An identifier cannot be used at the beginning of a declaration; it is valid only after the declaration end
12.3 VISIBILITY
procedure P (X: P); -- illegal
function Q (X: real := Q) return 0; -- illegal
procedure R (R: real); -- legal (although perhaps confusing)
constant k: integer := k*k; -- illegal constant t: t; -- illegal

## Slide 65
  Use Clause makes declarations in a package or library directly visible
  Using all makes all declarations visible
  Declarations can be hidden by homographs
  In case of explicit and implicit homographs, only the explicit one is visible
  Declarations in uninstantiated packages cannot be made visible
    use IEEE.std_logic_1164.all
    use work.my_package.all
    use work.my_package.my_function
12.4 USE CLAUSES

## Slide 66
  Overloading is when the same name or operator refers to different entities in different contexts
  Overload Resolution is the process used to select the correct meaning when multiple meanings are possible
  RULES
  Compatibility between names, expressions, and types
  Conformance between parameters and types
  Selecting the correct entity based on the context
12.5 THE CONTEXT OF OVERLOAD RESOLUTION

## Slide 67
13. DESIGN UNITS AND THEIR ANALYSIS
13.1 Design Units
13.2 Design Libraries
13.3 Context Declerations
13.4 Context Clauses
13.5 Order of Analysis
Chapter 13
Presenter:
Orhan Çalışkan

## Slide 68
  Independently analyzed constructs that are added to the design library
  Design file consists of multiple design units
  Primary Units: Core structures like entity declarations, package declarations, and context declarations
  Secondary Units: Bodies of primary units, such as architecture bodies
13.1 DESIGN UNITS
13.2 DESIGN LIBRARIES
  Design Library: An implementation-dependent storage area for design units. An application can support multiple design libraries
  Library Clause: Defines logical names for libraries in design units. If the same name is defined multiple times, only the first definition is valid.
  Working Library: The library where the library unit resulting from the analysis of a design unit is place
  Resource Library: Libraries that contain library units referenced in the analyzed design unit

## Slide 69
  Context Declaration: Defines context items that design units can reference
  Context Clause: Defines the initial name environment before the analysis of a design unit
    Scope: library_clause, use_clause, context_reference
      Library Clause: Defines the logical library names to be used in the design unit
      Use Clause: Makes certain declarations directly visible within the design unit
      Context Reference: References another context declaration
                context project_context is
                library project_lib;
                use project_lib.project_defs.all;
                library IP_lib;
                context IP_lib.IP_context;
                end context project_context;
13.3,4 CONTEXT DECLERATIONS / CONTEXT CLAUSE

## Slide 70
  The order of design unit analysis is based on visibility rules
  A primary unit must be analyzed before the design unit where its name is referenced
  A primary unit must be analyzed before its corresponding secondary unit, as the secondary unit depends on the primary unit
  In case of an error, the analysis is rejected and does not affect the working library
  A changed library unit may affect other units that reference its name
  A changed library unit becomes obsolete and must be reanalyzed before it can be used again
13.5 ORDER OF ANALYSIS

## Slide 71
14. ELABORATION AND EXECUTION
14.1 General
14.2 Elaboration of a Design Hierarchy
14.3 Elaboration of a Block, Package, Subprogram or Protected Type Header
14.4 Elaboration of a Declarative Part
14.5 Elaboration of a Statement Part
14.6 Dynamic Elaboration
14.7 Execution of a Model
Chapter 14
Presenter:
Seyit Koçak

## Slide 72
To execute a model, the design hierarchy is first elaborated, followed by the initialization of nets, and then the repetitive simulation cycle begins, during which processes are executed and nets are updated
14.1 GENERAL
14.2 ELABORATION OF A DESIGN HIERARCHY
Definition: Creates processes interconnected by nets, enabling simulation
Process:
  Executes vhpiCbStartOfElaboration and vhpiCbEndOfElaboration callbacks.Prepares block statements and implicit configurations for unbound components
Key Steps:
  Elaborates packages sequentially to resolve dependencies
  Configures PSL verification units after block elaboration
  Creates drivers and initializes scalar signals

## Slide 73
Describes the preparation of protected types, generics, subprograms, and ports, including their mapping and association. This ensures all components are properly initialized and ready for simulation
14.3 ELABORATION OF a BLOCK, PACKAGE, SUBPROGRAMS OR PROTECTED TYPE HEADER
14.4 ELABORATION OF A DECLARATIVE PART
Type definitions, subtypes, subprograms, and protected types are elaborated sequentially
. Attribute, configuration, and disconnection specifications are processed
Binding information, default values, and signal associations are properly established
14.5 ELABORATION OF A STATEMENT PART
Purpose:
  Ensure concurrent statements are correctly prepared for simulation
Concurrent Statements:
  All concurrent statements in a block are elaborated sequentially
Generate Statements:
  For-Generate: Creates blocks for each value in a specified range
  If-Generate: Creates a block if the condition evaluates to true; otherwise, no block is created
  Case-Generate: Creates a block for the matching alternative based on an evaluated expression
Component Instantiation: If bound to a design entity, the corresponding block is elaborated

## Slide 74
Definition:
  Dynamic elaboration occurs during simulation execution for constructs with sequential statements
Key Instances:
  Loop Statements: Loop parameters are elaborated, and the range is evaluated before execution
  Subprogram Calls: Parameters are elaborated and checked; exclusive access is required for protected or file operations
  Allocators: Subtype elaboration occurs before object allocation
  Sequential Blocks: Declarative parts are elaborated before block execution
14.6 DYNAMIC ELABORATION
14.7 EXECUTION OF A MODEL
Drivers: Handle signal value changes via transactions
Signal Updates: Compute and apply driving and effective values
Implicit Signals: Update signals like S'STABLE and S'QUIET per kernel rules

## Slide 75
13. Lexıcal elements
15.1 General
15.2 Character Set
15.3 Lexical Elements, Separators and Delimiters
15.4 Identifiers
15.5 Abstract Literals
15.6 Character Literals
15.7 String Literals
15.8 Bit String Literals
15.9 Comments
15.10 Reserved Words
15.11 Tools Directives
Chapter 15
Presenter:
Orhan Çalışkan

## Slide 76
15.1,2 GENERAL / CHARACTER SET
VHDL2019
VHDL2002

## Slide 77
15.3 LEXICAL ELEMENTS, SEPARATORS AND DELIMITERS
  Lexical Elements
    Identifiers
    Literals
    Delimiters and Separators
    Comments
  Delimiters
    Special Characters
  Separators
    Space
    End of Line
    Format Effectors

## Slide 78
  Basic identifiers are names used in VHDL to label objects
    Letters (A-Z, a-z)
    Digits (0-9)
    Underscore (_)
    Valid Examples : clk_100, my_signal1, raw_data, rst_n
    Invalid Examples : 100_clk, my-signal1, _rawdata
15.4 IDENTIFIERS
  Extended identifiers in VHDL are names that can include any graphic character
    Letters (A-Z, a-z)
    Digits (0-9)
    Special Characters (#, =, -, _ etc.)
    Space Characters
  Extended identifiers are case sensitive
  Extended identifiers must be wrap the backslashes(\)

## Slide 79
  Abstract Literals: Represent values in basic numerical types.
    Decimal Literals: Express numerical values (integer or fractional)
    Based Literals: Specify numerical values in a specific base (binary, octal, hexadecimal).
    Bit String Literals: Define numerical systems with specific bit sequences (B, O, X)
  Character Literals: Represent a single character
  String Literals: Represent a sequence of characters
    signal bit_signal : bit := ‘0’ ; -- Bit Literal
    signal bit_vector : bit_vector(7 downto 0) := x "128 " ; --Based Literals
    signal real_signal_pi : real := 3.14 ; -- Real Literal
    signal string_signal : string := "VHDL" ; -- String Literal
    signal another_char_signal : character := ‘1’ ; -- Character Literal
15.5,6,7,8 LITERALS

## Slide 80
    port
    (
    clk : in std_logic ;
    rst : in std_logic
    input_vld : in std_logic ;
    comm_input : in std_logic_vector (15 downto 0); --comm_input port is a slice name
    output_vld : in std_logic ;
    data_out : out std_logic_vector(15 downto 0) --data_out port is a slice name
    );
15.9 COMMENTS

## Slide 81
15.10 RESERVED WORDS
15.11 TOOL DIRECTIVE
  In VHDL, a tool directive is a command that directs a tool to perform a specific operation
  It starts with a backtick (`) and extends to the end of the line
  `define my_macro

## Slide 82
16.1 General
16.2 Predefined Attributes
16.3 Package STANDARD
16.4 Package TEXTIO
16.5 Standard Environment Package
16.6 Standard Mathematical Packages
16.7 Standard Multivalue Logic Package
16.8 Standard Synthesis Packages
16.9 Standard Synthesis Context Declarations
16.10 Fixed-point Package
16.11 Floating Point Package
16.12 Reflection Package
16. Predefıned language envıronment
Chapter 16
Presenter:
Mert Ecevit

## Slide 83
16.2 Predefined Attributes
https://www.hdlworks.com/hdl_corner/vhdl_ref/VHDLContents/AttributesPredefined.htm

## Slide 84
16.3 Package STANDARD
https://www.hdlworks.com/hdl_corner/vhdl_ref/VHDLContents/StandardPackage.htm

## Slide 85
16.4 Package TEXTIO
https://www.hdlworks.com/hdl_corner/vhdl_ref/VHDLContents/TEXTIOPackage.htm

## Slide 86
16.5 Standard Environment Package
The standard environmental package (ENV), which was introduced in VHDL-2008, has been extended with subprograms for reading and writing in directories on the native filesystem.
This package allows VHDL code to control the simulator, and to find out the simulator time resolution.
procedure stop(status:integer);
procedure stop;
procedure finish(status:integer);
procedure finish;
function resolution_limit return delay_length;
wait for env.resolution_limit;

## Slide 87
16.6 Standard Mathematical Packages
library IEEE;
Package MATH_REAL is
constant MATH_E : real := 2.71828_18284_59045_23536;
constant MATH_1_E: real := 0.36787_94411_71442_32160;
constant MATH_PI : real := 3.14159_26535_89793_23846;
constant MATH_1_PI : real := 0.31830_98861_83790_67154;
constant MATH_LOG_OF_2: real := 0.69314_71805_59945_30942;
constant MATH_LOG_OF_10: real := 2.30258_50929_94045_68402;
constant MATH_LOG2_OF_E: real := 1.44269_50408_88963_4074;
constant MATH_LOG10_OF_E: real := 0.43429_44819_03251_82765;
constant MATH_SQRT2: real := 1.41421_35623_73095_04880;
constant MATH_SQRT1_2: real := 0.70710_67811_86547_52440;
constant MATH_SQRT_PI: real := 1.77245_38509_05516_02730;
constant MATH_DEG_TO_RAD: real := 0.01745_32925_19943_29577;
constant MATH_RAD_TO_DEG: real := 57.29577_95130_82320_87685;
attribute FOREIGN : string;
function SIGN (X: real ) return real;
function CEIL (X : real ) return real;
function FLOOR (X : real ) return real;
function ROUND (X : real ) return real;
function FMAX (X, Y : real ) return real;
function FMIN (X, Y : real ) return real;
procedure UNIFORM (variable Seed1,Seed2:inout integer; variable X:out real);
function SQRT (X : real ) return real;
function CBRT (X : real ) return real;
function "**" (X : integer; Y : real) return real;
function "**" (X : real; Y : real) return real;
function EXP (X : real ) return real;
function LOG (X : real ) return real;
function LOG (BASE: positive; X : real) return real;
function SIN (X : real ) return real;
function COS ( X : real ) return real;
function TAN (X : real ) return real;
function ASIN (X : real ) return real;
function ACOS (X : real ) return real;
function ATAN (X : real) return real;
function ATAN2 (X : real; Y : real) return real;
function SINH (X : real) return real;
function COSH (X : real) return real;
function TANH (X : real) return real;
function ASINH (X : real) return real;
function ACOSH (X : real) return real;
function ATANH (X : real) return real;
end MATH_REAL;

## Slide 88
16.7 Standard Multivalue Logic Package
https://www.hdlworks.com/hdl_corner/vhdl_ref/VHDLContents/StdLogic1164.htm

## Slide 89
16.8 Standard Synthesis Packages
This subclause defines standard practices for synthesizing binary digital electronic circuits from VHDL source code
a) The hardware interpretation of values belonging to the BIT and BOOLEAN types defined in package STD.STANDARD and to the STD_ULOGIC type defined in package IEEE.STD_LOGIC_1164.
b) A function (STD_MATCH) that provides “don’t care” or “wild card” testing of values based on the STD_ULOGIC type.
c) Standard functions for representing sensitivity to the edge of a signal.
d) Packages that define one-dimensional array types for representing signed and unsigned arithmetic values, and that define arithmetic, shift, and type conversion operations on those types.
function STD_MATCH (L, R: STD_ULOGIC) return BOOLEAN; function STD_MATCH (L, R: STD_LOGIC_VECTOR) return BOOLEAN;
-- Result: termwise comparison per STD_LOGIC_1164 intent -- Result: terms compared per STD_LOGIC_1164 intent

## Slide 90
16.9 Standard Synthesis Context Declarations
library IEEE;
use IEEE.std_logic_1164.all;
use IEEE.numeric_std.all;
use sitelib.sitepack.all;
end context;
context proj1_context is -- compiled into library proj1lib
library sitelib;
context sitelib.site_context;
use proj1lib.proj1pack.all;
end context;
--call
library proj1lib;
context proj1lib.proj1_context;
16.10 Fixed-Point Package
16.11 Floating-Point Package
The library denoted by the library logical name IEEE contains packages FIXED_FLOAT_TYPES, FIXED_GENERIC_PKG, and FIXED_PKG
The library denoted by the library logical name IEEE contains packages FLOAT_GENERIC_PKG and FLOAT_PKG
16.12 Reflection Package
Package REFLECTION contains protected type declarations and access types to these protected types for a reflection API.

## Slide 91
17. VHDL Procedural Interface overview
Chapters 17,18,19
Presenter:
Furkan Kaya
18. VHPI access functions
19. VHPI information model

## Slide 92
VHPI Overview
Definition: VHPI (VHDL Procedural Interface) allows interaction between external tools and the VHDL simulation environment.
Purpose:
  Extend simulation functionality.
  Provide dynamic access to design objects.
Key Components:
  Handles: Represent simulation objects (e.g., signals, entities).
  Access Functions: Perform operations on these objects.
  Callbacks: Trigger actions on specific simulation events.
vhpi_register_cb(vhpiCbValueChange, signal_handle, my_callback);
CODE EXAMPLE

## Slide 93
VHPI Phases
Phases of Execution:
  Registration: Initialize callbacks and external tools.
  Simulation: Execute the design while interacting dynamically.
  Termination: Clean up and finalize external tool interactions.
procedure signal_monitor is
variable value: vhpiValueT;
begin
vhpi_get_value(signal_handle, value);
report "Signal value: " & value;
end;
CODE EXAMPLE

## Slide 94
Callbacks
vhpi_register_cb(vhpiCbTime, 50 ns, my_callback);
Purpose: Dynamically respond to events during simulation.
Types of Callbacks:
  Event-based: Triggered by signal changes or processes.
  Time-based: Activated after a specific time.
  Phase-based: Executed at specific simulation phases.
CODE EXAMPLE

## Slide 95
VHPI Data Types
signal_value: vhpiValueT;
vhpi_get_value(signal_handle, signal_value);
Definition: VHPI uses predefined data types to represent simulation data and interact with VHDL objects.
Key Data Types:
  vhpiInt: Integer type for indices and counters.
  vhpiReal: Real type for analog values or delays.
  vhpiString: Text-based data.
  vhpiValueT: Encapsulates values of signals and variables.
CODE EXAMPLE

## Slide 96
Data Access
signal_value.format := vhpiBinStr;
signal_value.value := "1101";
vhpi_put_value(signal_handle, signal_value, vhpiForce);
Purpose: Access and manipulate data during simulation.
Methods:
  Reading values using vhpi_get_value.
  Writing values using vhpi_put_value.
  Navigating objects using handles.
CODE EXAMPLE

## Slide 97
VHPI Object Model
signal_handle := vhpi_handle(vhpiSignal, architecture_handle);
Definition: Represents the hierarchical structure of VHDL designs, enabling navigation and manipulation of components.
Key Objects:
  Signals: Data carriers between components.
  Variables: Local storage within processes.
  Processes: Describe behavior.
  Components: Instances of entities.
CODE EXAMPLE

## Slide 98
Object Hierarchy
root_handle := vhpi_handle(vhpiRoot, null);
entity_handle := vhpi_handle_by_name("MyEntity", root_handle);
Structure:
  Designs are organized hierarchically, starting from root objects.
  Parent-child relationships allow traversal between components.
Usage:
  Retrieve handles for signals, processes, or variables.
  Navigate design hierarchy dynamically.
CODE EXAMPLE

## Slide 99
Signal Interaction
signal_value.value := "0000";
vhpi_put_value(signal_handle, signal_value, vhpiInertial);
Purpose: Manage signal behavior during simulation.
Actions:
  Monitor signal value changes.
  Modify signal values dynamically to simulate specific scenarios.
CODE EXAMPLE

## Slide 100
Process and Component Interaction
process_handle := vhpi_handle(vhpiProcess, entity_handle);
vhpi_set_disable(process_handle, true);
Purpose: Interact with processes and components during runtime.
Actions:
  Activate or deactivate processes.
  Modify or monitor component behavior.
CODE EXAMPLE

## Slide 101
Advanced Use Cases
vhpi_register_cb(vhpiCbAfter, 100 ns, my_callback);
vhpi_get_value(signal_handle, signal_value);
Applications:
  Debugging and monitoring signals.
  Automating tests with dynamic modifications.
  Interfacing with external tools for co-simulation.
CODE EXAMPLE

## Slide 102
20. VHPI Tool execution
Chapters 20,21,22
Presenter:
Koray Karakurt
21. VHPI CAllbacks
22. VHPI VALUE ACCESS AND UPDATE

## Slide 103
  This chapter describes the way in which foreign models and applications interact with a VHPI tool and the way in which the tool executes VHDL and foreign models
  A foreign model is a design entity whose architecture is decorated with the 'FOREIGN attribute in the form described in this clause, or a subprogram similarly decorated
  A foreign application is a VHPI program that does not correspond to design entities or subprograms declared in the VHDL model
  The VHPI supports various execution phases of a VHDL tool
  Each phase is identified by a value of the enumeration type vhpiPhaseT
  A VHPI program determines the current phase of the VHDL tool by calling the VHPI routine vhpi_get supplying the value vhpiPhaseP as the first parameter and NULL as the second parameter and the return value of vhpi_get is one of the values of vhpiPhaseT
20. VHPI TOOL EXECUTION
20.1 General

## Slide 104
In temporal order, the VHDL tool execution phases are:
20.2 vhpiRegistrationPhase: indicates the tool has begun executing
  Foreign models, applications, and libraries of foreign models are registered
  Each registered and enabled vhpiCbStartOfTool callback is executed
20.3 vhpiAnalysisPhase: The analysis of a design file is occurring
  Each registered and enabled vhpiCbStartOfAnalysis callback is executed
  One or more design files are analyzed (the manner is not specified by this standard)
  Each registered and enabled vhpiCbEndOfAnalysis callback is executed
20.4 vhpiElaborationPhase: The static elaboration of a design hierarchy is occurring
  Each registered and enabled vhpiCbStartOfElaboration callback is executed
  The design hierarchy is elaborated
  Each registered and enabled vhpiCbEndOfElaboration callback is executed
20.5 vhpiInitializationPhase: The initialization of an elaborated design hierarchy is occurring
20.6 vhpiSimulationPhase: The execution of an elaborated and initialized design hierarchy is occurring
20. VHPI TOOL EXECUTION

## Slide 105
  20.7 vhpiSavePhase: The current state of a VHDL model is being saved for possible restart
    The tool performs some actions, not specified by this standard, to save the current state of the VHDL model, which includes the time of the next simulation cycle, Tn.
    Each registered and enabled vhpiCbStartOfSave callback is executed
    Each registered and enabled vhpiCbEndOfSave callback is executed
  20.8 vhpiRestartPhase: A previously saved VHDL model is being restarted from the point of its save
    The tool performs some actions, not specified by this standard, to restore the previously saved state of the VHDL model, including the time of the next simulation cycle, Tn (the manner is not specified by this standard)
    Each registered and enabled vhpiCbStartOfRestart callback is executed
    Each registered and enabled vhpiCbEndOfRestart callback is executed
  20.9 vhpiResetPhase: A VHDL model is being restarted from the state it was in at the end of initialization
    Each registered and enabled vhpiCbStartOfReset callback is executed
    All callbacks except vhpiCbEndOfReset callbacks are removed
    The projected output waveform of each driver is reset to its initial contents
    The current time, Tc, is reset to be 0 ns
    Each registered and enabled vhpiCbEndOfReset callback is executed
  20.10 vhpiTerminationPhase: The tool is terminating
20. VHPI TOOL EXECUTION

## Slide 106
  A callback is a mechanism for a VHPI program to gain control during tool execution
  A VHPI program registers a callback, providing to the tool a reference to a callback function and a callback reason, specification of an event or events that may trigger execution of the callback function by the tool
  Depending on the callback reason, a callback is either a one-time callback, meaning that the callback function is triggered at most once, or a repetitive callback, meaning that the callback function may be triggered multiple times
  A callback is in one of three states:
    Enabled = the callback function will be called if the trigger event occurs
    Disabled = the callback function will not be called if the trigger event occurs
    Mature = the callback is a one-time callback whose trigger event has occurred
21. VHPI CALLBACKS
21.1 General

## Slide 107
  A callback is represented in the VHPI information model by an object of class callback
  A VHPI program can obtain a handle to a callback object by navigating the information model
  The VHPI provides functions to register, remove, enable, and disable callbacks and to access information about callbacks
21. VHPI CALLBACKS
21.2 Callback Functions
21.3 Callback Reasons
  Callback reasons are identified by enumeration constants, defined in the VHPI include file, whose names start with the characters vhpiCb
  The term callback qualified with an enumeration constant identifying a callback reason refers to a callback that is registered with the reason identified by the enumeration constant
  This subclause specifies the values required, if any, in the obj, time, and value members of the callback data structure provided by a VHPI program upon registration of a callback for each reason
  If a VHPI program provides a pointer to a time structure in the time member of a callback data structure, the VHPI program shall allocate the memory for the time structure
  Similarly, if a VHPI program provides a pointer to a value structure in the value member of a callback data structure, the VHPI program shall allocate the memory for the value structure

## Slide 108
  Describes the data structures and operations provided in the VHPI for reading and updating values of objects in a VHDL model
  The VHPI header file (see Annex B) defines a number of data types that are used by VHPI function which are described in this subclause (22.2)
  It is an error if a VHPI program uses a given type described in this clause to represent a VHDL scalar type, and there are position numbers in the scalar type that exceed the range of position numbers that can be represented in the given type
  A VHPI program may read the value of certain objects in the design hierarchy information model using the vhpi_get_value function (see 23.19)
  The objects for which it is legal to read the value are: an object of class name or driver or transaction or port or literal or expr
22. VHPI Value Access and Update
22.1 General
22.2 Value Structures and types
22.3 Reading Object Values

## Slide 109
  For each type of object whose value can be read using the vhpi_get_value function, there is a native format, defined as follows:
22. VHPI Value Access and Update
22.4 Formatting values

## Slide 110
22. VHPI Value Access and Update
22.5 Updating object values
  A VHPI program may update the value of certain objects in the design hierarchy information model using the vhpi_put_value function (see 23.28)
  The objects for which it is legal to update the value are:
    An object of one of the following subclasses of objDecl: genericDecl, sigDecl, varDecl, portDecl, sigParamDecl, or varParamDecl
    An object of class aliasDecl whose target object of the aliasedName association is an object for which it is legal to update the value
    An object of one of the following subclasses of prefixedName: indexedName, sliceName, or selectedName, provided the target object of the prefix association is an object for which it is legal to update the value
    An object of class derefObj
    An object of class driver
    An object of class port
    An object of class funcCall

## Slide 111
22. VHPI Value Access and Update
22.6 Scheduling transactions on drivers
  A VHPI program may schedule a transaction on a driver or transactions on drivers in a collection of drivers using the vhpi_schedule_transaction function (see 23.34)
  The effect of scheduling a transaction on a driver is to modify the projected output waveform of the driver according to the rules described in 10.5.2.2
  The value provided for each driver in a value structure to the vhpi_schedule_transaction function is used as the value component of a transaction assigned to the driver
  The time component of the transaction and the delay mechanism are determined as described in 23.34

## Slide 112
23. Vhpı functıon reference
Chapter 23
Presenter:
Orhan Çalışkan

## Slide 113
    int vhpi_assert(vhpiSeverityT severity, char *formatmsg, ...);
      The vhpi_assert function in VHDL works like the report statement, using a format string (similar to printf) and a severity argument to generate a formatted message with a severity level
    int vhpi_check_error (vhpiErrorInfoT *error_info_p);
      The vhpi_check_error function checks if the previous VHPI function call raised an error. It takes an argument, error_info_p, which is either a pointer to an error information structure or NULL
    int vhpi_compare_handles (vhpiHandleT handle1, vhpiHandleT handle2);
      Determines whether the arguments handle1 and handle2 refer to the same object
      1 if handle1 and handle2 refer to the same object, or 0 otherwise
23 VHPI FUNCTION REFERENCE

## Slide 114
    int vhpi_control (vhpiSimControlT command, ...);
      The vhpi_control function requests specific control actions for a VHPI tool
      vhpiStop: Stops the simulation and waits for further commands
      vhpiFinish: Enters the termination phase of the simulation
      vhpiReset: Enters the reset phase of the simulation
      If the command is not one of these, the tool performs a custom action
    vhpiHandleT vhpi_create (vhpiClassKindT kind, vhpiHandleT handle1,
    vhpiHandleT handle2);
      The vhpi_create function is used to create VHPI objects of specific classes, such as processStmt or driver, based on the kind argument
      It associates the created objects with other VHPI objects and sets certain properties (like IsForeign) to default values
23 VHPI FUNCTION REFERENCE

## Slide 115
    vhpiIntT vhpi_get(vhpiIntPropertyT property, vhpiHandleT object);
      The function disables an enabled callback, preventing the callback function from executing when the trigger event occurs
      It returns the property value if readable, or vhpiUndefined if the property cannot be read
    size_t vhpi_get_data(int32_t id, void * dataLoc, size_t numBytes);
      The vhpi_get_data function reads a specified number of bytes from a saved data set and writes them to dataLoc
      It continues reading from the last location on subsequent calls and writes zeros if fewer bytes remain than requested
    int vhpi_get_foreignf_info (vhpiHandleT hdl, vhpiForeignDataT *foreignDatap);
      The vhpi_get_foreignf_info function retrieves details about a foreign model or application, such as its type, functions, and names, and stores them in the foreignDatap structure. It returns 0 on success or 1 on error
23 VHPI FUNCTION REFERENCE

## Slide 116
    int vhpi_get_next_time (vhpiTimeT *time_p);
      The vhpi_get_next_time function writes the time of the next simulation cycle (Tn) to a provided time structure. It returns vhpiNoActivity if no further simulation activity exists, 0 if successful, or a non-zero value on error
    vhpiPhysT vhpi_get_phys (vhpiPhysPropertyT property, vhpiHandleT object);
      The vhpi_get_physical_property function retrieves the value of a specified physical property for a given object. It returns the property value if readable or an unspecified value otherwise
    vhpiRealT vhpi_get_real (vhpiRealPropertyT property, vhpiHandleT object);
      The vhpi_get_real_property function retrieves the value of a specified real property for a given object. It returns the property value if readable or an unspecified value otherwise
23 VHPI FUNCTION REFERENCE

## Slide 117
    const vhpiCharT * vhpi_get_str (vhpiStrPropertyT property, vhpiHandleT object);
      The vhpi_get_str_property function retrieves the value of a specified string property for a given object. It returns a pointer to the string if readable or NULL otherwise
    void vhpi_get_time (vhpiTimeT *time_p, long *cycles);
      The vhpi_get_time function retrieves the current simulation time and/or the number of delta or total simulation cycles. It writes these values to provided pointers and returns no value
    int vhpi_get_value (vhpiHandleT expr, vhpiValueT *value_p);
      The vhpi_get_value function formats and retrieves the value of the object referred to by expr. It returns 0 on success, required storage size if space is insufficient, or a negative value on error
23 VHPI FUNCTION REFERENCE

## Slide 118
    vhpiHandleT vhpi_handle (vhpiOneToOneT type, vhpiHandleT referenceHandle);
      The vhpi_handle function retrieves the target object of a one-to-one association based on type and referenceHandle. It returns a handle to the target object if one exists or NULL otherwise
    vhpiHandleT vhpi_handle_by_index (vhpiOneToManyT itRel, vhpiHandleT parent, int32_t indx);
      The vhpi_handle_by_index function retrieves a target object from an ordered one-to-many association using itRel, parent, and indx. It returns a handle to the target object at the specified index or NULL if no such object exists
    vhpiHandleT vhpi_handle_by_name (const char *name, vhpiHandleT scope);
      The vhpi_handle_by_name function searches for an object by its FullName using the name string and optional scope. It returns a handle to the found object or NULL if not found
23 VHPI FUNCTION REFERENCE

## Slide 119
    int vhpi_is_printable( char ch )
      The function checks if the character code of the ch argument represents a graphic character. Return 1 if it's a graphic character, 0 otherwise
    vhpiHandleT vhpi_iterator (vhpiOneToManyT type, vhpiHandleT referenceHandle);
      The function creates an iterator object for a one-to-many association if target objects exist and returns a handle to the iterator. If no target objects exist, it returns NULL
    int vhpi_printf (const char *format, ...);
      The function writes a formatted string to one or more tool output files based on a format string and arguments, similar to the C printf function. It returns the number of characters written, or -1 if an error occurs
23 VHPI FUNCTION REFERENCE

## Slide 120
    int vhpi_protected_call (vhpiHandleT varHdl, vhpiUserFctT userFct, void *userData);
      The vhpi_protected_call function ensures exclusive access to a varDecl object with specific properties and calls the user function with the object handle and user data. It returns the value from the user function
    size_t vhpi_put_data (int32_t id, void * dataLoc, size_t numBytes);
      The vhpi_put_data function writes bytes from dataLoc to the saved data set identified by id. It returns the number of bytes written, or 0 if the write fails,
    int vhpi_put_value (vhpiHandleT object, vhpiValueT *value_p, vhpiPutValueModeT mode);
      The object argument is a handle to an object or function with a foreign subprogram. The value_p specifies the value to update, and mode determines the update method. The function returns 0 if successful, or a non-zero value if there's an error.
23 VHPI FUNCTION REFERENCE

## Slide 121
    vhpiHandleT vhpi_register_cb (vhpiCbDataT *cb_data_p, int32_t flags);
      The cb_data_p argument is a pointer to the callback data, and flags specify the registration mode. The function registers a callback and returns a handle if vhpiReturnCb is set, or NULL if cleared. If vhpiDisableCb is set, the callback is disabled; otherwise, it's enabled. The function does not retain references after execution
    vhpiHandleT vhpi_register_foreignf (vhpiForeignDataT *foreignDatap);
      The foreignDatap argument is a pointer to a foreign data structure for registration, specifying the foreign entity type with kind and including function pointers for elaboration (elabf) and execution (execf). It also includes libraryName and modelName for the object and model names. The function registers the foreign entity and returns a handle if successful, or NULL on Error
    int vhpi_release_handle (vhpiHandleT object);
      The object argument is a handle referring to an object. The function releases the handle and returns 0 if successful, or 1 if an error occurs
23 VHPI FUNCTION REFERENCE

## Slide 122
    int vhpi_remove_cb (vhpiHandleT cb_obj);
      The cb_obj argument is a handle to a registered callback. The function removes the callback, invalidating the handle. It returns 0 if successful, or 1 if an error occurs
    vhpiHandleT vhpi_scan (vhpiHandleT iterator);
      The iterator argument is a handle to an iterator object. If the iterator has no element at its position, the handle is released and NULL is returned. Otherwise, a handle to the current element is returned, and the iterator moves to the next element. The return value is either a handle or NULL
23 VHPI FUNCTION REFERENCE

## Slide 123
    int vhpi_schedule_transaction (vhpiHandleT drivHdl, vhpiValueT *value_p,uint32_t numValues, vhpiTimeT *delayp, vhpiDelayModeT delayMode, vhpiTimeT *pulseRejp);
      drivHdl refers to a driver or driverCollection. value_p is a pointer to value structures, and numValues is the count. Transactions are scheduled with a relative delay (delayp), and delayMode specifies the type (inertial or transport)
      If delayMode is inertial, pulseRejp sets the pulse rejection limit; otherwise, it's ignored. If pulseRejp is NULL, the limit equals the delay
      Return 0 if successful, non-zero if error occurs
    int vhpi_vprintf (const char *format, va_list args);
      The format argument is a pointer to a format string with conversion codes, as per ISO/IEC 9899:2018 for the C vprintf function. It formats a string to be written to output files
      Return value: The number of characters written, or -1 if an error occurs
23 VHPI FUNCTION REFERENCE

## Slide 124
24. STANDARD TOOL DIRECTIVES
24.1 Protect Tool Directives
24.2 Conditional Analysis Tool Directives
Chapter 24
Presenter:
Seyit Koçak

## Slide 125
Encrypt VHDL designs to prevent text disclosure while allowing authorized tools to process the design
Key Elements:
  Encryption Envelope: Encrypted text and instructions
  Decryption Envelope: Details for decryption
24.1 PROTECT TOOL DIRECTIVES
24.2 CONDITIONAL ANALYSIS TOOL DIRECTIVES
Purpose: Allows conditional inclusion/exclusion of VHDL description parts based on tool or user settings
Key Elements:
  Warning: Adds a warning message, does not stop analysis
  Error: Stops analysis with an error message
Tool-Supplied Identifiers:
  VHDL_VERSION: VHDL version (e.g., "2008")
  TOOL_TYPE: Tool type (e.g., "SIMULATION")
  TOOL_NAME/EDITION/VERSION: Tool-specific details
  .

## Slide 126
www.youtube.com/@falsepaths
End of IEEE 1076 – 2019 Standard
VHDL Project Closure Presentation
THANKS
Furkan Kaya,
Mert Ecevit,
Orhan Çalışkan,
Seyit Koçak
Yunus Küçük