## Slide 1: A Summary of 1076 - 2019 IEEE Standard VHDL Language Reference Manual
by Furkan Kaya, Koray Karakurt,
Mert Ecevit, Orhan Çalışkan, Seyit Koçak and Yunus Küçük
27/12/2024

## Slide 2
3.1 General
3.2 Entity Declarations
3.3 Architecture Bodies
3.4 Configuration Declarations
3. Design entities & configurations
Chapter 3
Presenter:
Furkan Kaya

## Slide 3
Design
Architecture
3.1 GENERAL
3.2 ENTITY DECLARATIONS

## Slide 4
CODE EXAMPLE
library IEEE;
use IEEE.std_logic_1164.all;
use IEEE.numeric_std.all;
entity generic_adder is
generic
(
data_width : integer := 32
);
port
(
input_a : in std_logic_vector (data_width-1 downto 0);
input_b : in std_logic_vector (data_width-1 downto 0);
output_adder : out std_logic_vector (data_width downto 0)
);
end generic_adder;
architecture behavioral of generic_adder is
signal output_internal : signed (output_adder'range);
begin
output_internal <= signed(input_a) + signed(input_b);
output_adder <= std_logic_vector(output_internal);
end architecture behavioral;

## Slide 5
4. Subprograms & packages
4.1 General
4.2 Subprogram Declarations
4.3 Subprogram Bodies
4.4 Subprogram Instantiation Declarations
4.5 Subprogram Overloading
4.6 Resolution Functions
4.7 Package Declarations
4.8 Package Bodies
4.9 Package Instantiation Declarations
4.10 Conformance Rules
Chapter 4
Presenter:
Seyit Koçak

## Slide 6
Subprograms define algorithms through procedures and functions, serving to compute values or perform actions
Procedures are subprograms that execute a series of statements to perform actions but do not return a value. They are called as statements and can modify the state of the program
Functions are classified as pure or impure
Packages separate the declarations and bodies of these subprograms, allowing common resources to be shared
4.1 GENERAL
4.2 SUBPROGRAM DECLERATİONS
Subprogram declarations define procedures or functions by specifying their designator, parameters, generics (if any), and for functions, the return type and whether it is pure or impure
Procedures are always identified by a name, while functions can also be identified by operator symbols, enabling operator overloading
Functions return a value, whereas procedures execute actions without returning any value and can modify external variables or signals.
-

## Slide 7
4.2 SUBPROGRAM DECLERATİONS

## Slide 8
CODE EXAMPLE
library IEEE;
use IEEE.STD_LOGIC_1164.ALL;
use IEEE.NUMERIC_STD.ALL;
procedure UpdateValue(signal clk : in STD_LOGIC; signal reset : in STD_LOGIC;
signal data_in : in STD_LOGIC_VECTOR(7 downto 0);
signal data_out : out STD_LOGIC_VECTOR(7 downto 0)) is
Begin
if reset = '1' then
data_out <= (others => '0’);
elsif rising_edge(clk) then
data_out <= data_in;
end if;
end procedure;
entity ProcedureWithClock is
Port (
clk : in STD_LOGIC;
reset : in STD_LOGIC;
data_in : in STD_LOGIC_VECTOR(7 downto 0);
data_out : out STD_LOGIC_VECTOR(7 downto 0) );
end ProcedureWithClock;
architecture Behavioral of ProcedureWithClock is
begin
process(clk, reset)
begin
UpdateValue(clk, reset, data_in, data_out);
end process;
end Behavioral;

## Slide 9
4.2 SUBPROGRAM DECLARATİONS
Pure Functions
  Pure functions always return the same output for the same input values.
Impure Functions
  Impure functions may produce different outputs for the same inputs or modify external variables or signals
Constant parameters allow read-only access, while variable parameters allow both reading and writing of values during subprogram execution.
Signal parameters pass references to signals, their drivers, or both into the subprogram call. Assignments to signal parameters directly affect the actual signal drivers associated with them.

## Slide 10
4.3 SUBPROGRAM BODIES
Subprogram bodies define the execution logic of a subprogram and specify the operations it performs.
A body consists of three main parts: specification (definition of parameters and type), declarative part (variables, constants, or nested subprograms), and statement part (sequential operations).
Except for foreign subprograms, the body is executed when the subprogram is called, using the provided parameters to carry out its tasks.
4.4 SUBPROGRAM INSTANTIATION DECLARATIONS
Subprogram instantiation declaration takes a general template of a subprogram (uninstantiated subprogram) and customizes it into an independent version (instantiated subprogram) with specific parameters or generics.
This method enhances reusability and allows the same subprogram to be used in different scenarios with different configurations.
During instantiation, the parameters or generics must match the profile of the original uninstantiated subprogram.

## Slide 11
CODE EXAMPLE
library IEEE;
use IEEE.STD_LOGIC_1164.ALL;
use IEEE.NUMERIC_STD.ALL;
function Add(a, b: INTEGER) return INTEGER is
begin
return a + b;
end Add;
function PositiveAdd is new Add;
entity SubprogramInstantiationExample is
Port (
a, b : in INTEGER;
result : out INTEGER
);
end SubprogramInstantiationExample;
architecture Behavioral of SubprogramInstantiationExample is
begin
process(a, b)
begin
if (a > 0 and b > 0) then
result <= PositiveAdd(a, b);
else
result <= 0;
end if;
end process;
end Behavioral;

## Slide 12
4.5 SUBPROGRAM OVERLOADING
Subprogram overloading allows multiple subprograms with the same name to coexist, distinguished by their parameter types, order, and count, or by the function's return type.
A subprogram call is ambiguous if the provided parameters and their types are not sufficient to uniquely identify one specific subprogram.
Operators like +, -, and, and or can also be overloaded, allowing both unary and binary implementations for the same operator.
4.6 RESOLUTION FUNCTIONS
A resolution function determines how values from multiple sources for a single signal are combined into one resolved value.
It must be a pure function with a single input parameter, which is an array representing the multiple sources, and a return type matching the signal's type.
Resolution functions are implicitly called during simulation cycles whenever their associated signals are active.

## Slide 13
4.7,8,9 PACKAGE DECLARATIONS,BODIES,INSTANTIATION
Package declarations define the interface of a package, including constants, types, subprograms, and generics.
Items declared in a package can be made visible in other design units through selection or use clauses.
A package body must match its corresponding package declaration and follow it in the same declarative region.
Package instantiation declarations create an instance of an uninstantiated package, associating actuals with generics through a generic map aspect.
The instance behaves like a generic-mapped package with declarations and bodies from the uninstantiated package.

## Slide 14
CODE EXAMPLE
library IEEE;
use IEEE.STD_LOGIC_1164.ALL;
package MyPackage is
constant DEFAULT_VALUE: integer := 10;
function Double(Value: integer) return integer;
end package MyPackage;
package body MyPackage is
function Double(Value: integer) return integer is
begin
return Value * 2;
end function Double;
end package body MyPackage;
Port (
InputValue : in integer;
OutputValue : out integer
);
end PackageExample;
architecture Behavioral of PackageExample is
use work.MyPackage.all;
begin
process(InputValue)
begin
OutputValue <= Double(InputValue);
end process;
end Behavioral;

## Slide 15
4.10 CONFORMANCE RULES
A numeric literal in a subprogram specification can be replaced by another numeric literal only if they represent the same value.Example: procedure P(X: INTEGER := 10) is equivalent to procedure P(X: INTEGER := 10.0) (since 10 and 10.0 represent the same value).
A simple name in a subprogram can be replaced by an expanded name, but only if both names refer to the same declaration.Example: If Q is declared inside P, then Q.R is equivalent to P.Q.R.
A pure function specification is never conformant with an impure function specification.
  Example: Pure functions cannot modify external signals, while impure functions can.

## Slide 16
CODE EXAMPLE
library IEEE;
use IEEE.std_logic_1164.all;
use IEEE.numeric_std.all;
entity generic_adder is
generic
(
data_width : integer := 32
);
port
(
input_a : in std_logic_vector (data_width-1 downto 0);
input_b : in std_logic_vector (data_width-1 downto 0);
output_adder : out std_logic_vector (data_width downto 0)
);
end generic_adder;
architecture behavioral of generic_adder is
signal output_internal : signed (output_adder'range);
begin
output_internal <= signed(input_a) + signed(input_b);
output_adder <= std_logic_vector(output_internal);
end architecture behavioral;

## Slide 17
www.youtube.com/@falsepaths
End of IEEE 1076 – 2002 Standard
VHDL Project Closure Presentation
THANKS
Furkan Kaya,
Mert Ecevit,
Orhan Çalışkan,
Seyit Koçak
Yunus Küçük