## Slide 1: A Summary of 1076 - 2019 IEEE Standard VHDL Language Reference Manual
by Furkan Kaya, Koray Karakurt,
Mert Ecevit, Orhan Çalışkan, Seyit Koçak and Yunus Küçük
27/12/2024

## Slide 2
3.1 General
3.2 Entity Declarations
3.3 Architecture Bodies
3.4 Configuration Declarations
3. Design entities & configurations
Chapter 3
Presenter:
Furkan Kaya

## Slide 3
3.1 GENERAL
3.2 ENTITY DECLARATIONS | 3.3 ARCHITECTURE BODIES | 3.4 CONFIGURATION DECLARATIONS
Design Entity:
  Entity declaration
  Architecture bodies
  Configuraiton decleration
An entity in VHDL defines the external interface of a design.
entity Full_Adder is
port ( X, Y, Cin: in Bit;
Cout, Sum: out Bit
);
end Full_Adder;
entity AndGate is
generic (
N: Natural := 2
)
port(
inputs : in bit_vector (1 to N);
result : out bit
);
end entity AndGate;
entity TestBench is
end TestBench;
An architecture in VHDL describes the internal implementation of an entity.
architecture Behavioral of SENSOR_CNTRLLR is
component I2C_master is
...
end component I2C_master;
constant POR_LIM : integer := 99_999;
type SENSOR_STATES is (
POR_WAIT,CONFIG_SENSOR, TAKE_DATA,BFT_WAIT
);
signal sensor_ctrl_state : SENSOR_STATES;
signal por_cnt : integer range 0 to POR_LIM;
begin ...
A configuration in VHDL specifies how components within an architecture are bound to entities and architectures.
library TTL, Work;
configuration V4_27_87 of Processor is
use Work.all;
for Structure_View
for A1: ALU
use configuration TTL.SN74LS181;
end for;
for M1,M2,M3: MUX
use entity Multiplex4 (Behavior);
end for;
for all: Latch
-- use defaults
end for;
end for;
end configuration V4_27_87;
Examples 1 and 3 taken from "IEEE1076-2019" document where example 2 is my example.
EX-1
EX-3
EX-2

## Slide 4
CODE EXAMPLE
library IEEE;
use IEEE.std_logic_1164.all;
use IEEE.numeric_std.all;
entity generic_adder is
generic
(
data_width : integer := 32
);
port
(
input_a : in std_logic_vector (data_width-1 downto 0);
input_b : in std_logic_vector (data_width-1 downto 0);
output_adder : out std_logic_vector (data_width downto 0)
);
end generic_adder;
architecture behavioral of generic_adder is
signal output_internal : signed (output_adder'range);
begin
output_internal <= signed(input_a) + signed(input_b);
output_adder <= std_logic_vector(output_internal);
end architecture behavioral;

## Slide 5
4. Subprograms & packages
4.1 General
4.2 Subprogram Declarations
4.3 Subprogram Bodies
4.4 Subprogram Instantiation Declarations
4.5 Subprogram Overloading
4.6 Resolution Functions
4.7 Package Declarations
4.8 Package Bodies
4.9 Package Instantiation Declarations
4.10 Conformance Rules
Chapter 4
Presenter:
Seyit Koçak

## Slide 6
Subprograms define algorithms through procedures and functions, serving to compute values or perform actions
Procedures are subprograms that execute a series of statements to perform actions but do not return a value. They are called as statements and can modify the state of the program
Functions are classified as pure or impure
Packages separate the declarations and bodies of these subprograms, allowing common resources to be shared
4.1 GENERAL
4.2 SUBPROGRAM DECLERATİONS
Subprogram declarations define procedures or functions by specifying their designator, parameters, generics (if any), and for functions, the return type and whether it is pure or impure
Procedures are always identified by a name, while functions can also be identified by operator symbols, enabling operator overloading
Functions return a value, whereas procedures execute actions without returning any value and can modify external variables or signals
-

## Slide 7
CODE EXAMPLE
library IEEE;
use IEEE.std_logic_1164.all;
use IEEE.numeric_std.all;
entity procedurewithclock is
port (
clk : in std_logic;
reset : in std_logic;
data_in : in std_logic_vector(7 downto 0);
data_out : out std_logic_vector(7 downto 0)
);
end procedurewithclock;
architecture behavioral of procedurewithclock is
procedure updatevalue(
signal clk : in std_logic;
signal reset : in std_logic;
signal data_in : in std_logic_vector(7 downto 0);
variable data_out : inout std_logic_vector(7 downto 0)
) is
begin
if reset = '1' then
data_out := (others => '0');
elsif rising_edge(clk) then
data_out := data_in;
end if;
end procedure;
begin
process(clk, reset)
variable temp_data : std_logic_vector(7 downto 0);
begin
updatevalue(clk, reset, data_in, temp_data);
data_out <= temp_data;
end process;
end behavioral;

## Slide 8
4.2 SUBPROGRAM DECLARATİONS
Pure functions always return the same output for the same input values
Impure functions may produce different outputs for the same inputs or modify external variables or signals
Constant parameters allow read-only access, while variable parameters allow both reading and writing of values during subprogram execution.
Signal parameters pass references to signals, their drivers, or both into the subprogram call Assignments to signal parameters directly affect the actual signal drivers associated with them
4.3 SUBPROGRAM BODIES
A body consists of three main parts: specification (definition of parameters and type), declarative part (variables, constants, or nested subprograms), and statement part (sequential operations)
4.4 SUBPROGRAM INSTANTIATION DECLARATIONS
Subprogram instantiation customizes a general subprogram template into an independent version with specific parameters or generics

## Slide 9
CODE EXAMPLE
library IEEE;
use IEEE.std_logic_1164.all;
use IEEE.numeric_std.all;
package my_subprograms is
function add_integer(a, b: integer) return integer;
end my_subprograms;
package body my_subprograms is
function add_integer(a, b: integer) return integer is
begin
return a + b;
end add_integer;
end my_subprograms;
use work.my_subprograms.all;
entity subprograminstantiationexample is
port (
a, b : in integer;
c, d : in integer;
result_int : out integer;
result_real: out integer
);
end subprograminstantiationexample;
architecture behavioral of subprograminstantiationexample is
constant threshold : integer := 10;
begin
process(a, b, c, d)
variable tempresultint : integer; --temporary storage
variable tempresultreal : integer;
begin
if (a > threshold and b > threshold) then
tempresultint := add_integer(a, b);
result_int <= tempresultint;
else
result_int <= 0;
end if;
if (c > threshold and d > threshold) then
tempresultreal := add_integer(c, d);
result_real <= tempresultreal;
else
result_real <= 0;
end if;
end process;
end behavioral;

## Slide 10
4.7,8,9 PACKAGE DECLARATIONS,BODIES,INSTANTIATION
Package declarations define the interface of a package, including constants, types, subprograms, and generics
Items declared in a package can be made visible in other design units through selection or use clauses
A package body must match its corresponding package declaration and follow it in the same declarative region
Package instantiation declarations create an instance of an uninstantiated package, associating actuals with generics through a generic map aspect
The instance behaves like a generic-mapped package with declarations and bodies from the uninstantiated package
library IEEE;
use IEEE.std_logic_1164.all;
package mypackage is
constant default_value: integer := 10;
function double(value: integer) return integer;
function triple(value: integer) return integer;
end package mypackage;
package body mypackage is
function double(value: integer) return integer is
begin
return value * 2;
end function double;
function triple(value: integer) return integer is
begin
return value * 3;
end function triple;
end package body mypackage;
entity packageexample is
port (
inputvalue : in integer;
outputvalue : out integer;
triplevalue : out integer
);
end packageexample;
architecture behavioral of packageexample is
use work.mypackage.all;
begin
process(inputvalue)
begin
outputvalue <= double(inputvalue);
triplevalue <= triple(inputvalue);
end process;
end behavioral;
CODE EXAMPLE

## Slide 11
5. tYPES
5.1 General
5.2 Scalar Types
5.3 Composite Types
5.4 Access Types
5.5 File Types
5.6 Protected Types
5.7 String Representations
5.8 Unspecified Types
Chapter 5
Presenter:
Seyit Koçak

## Slide 12
A type is defined by a set of values and operations, including basic and predefined operations automatically provided
Composite types can be unconstrained, fully constrained, or partially constrained
Types are divided into five main categories: scalar, composite, access, file, and protected types
5.1 GENERAL
5.2 SCALAR TYPES

## Slide 13
CODE EXAMPLE
library ieee;
use ieee.std_logic_1164.all;
use ieee.numeric_std.all;
entity bcdtoseven is
port (
sw : in std_logic_vector(13 downto 0);
clk : in std_logic;
seg : out std_logic_vector(6 downto 0);
an : out std_logic_vector(3 downto 0)
);
end bcdtoseven;
architecture behavioral of bcdtoseven is
type digit_type is (ones_digit, tens_digit, hundreds_digit, thousands_digit);
signal current_digit : digit_type := ones_digit;
signal ones, tens, hundreds, thousands : std_logic_vector(3 downto 0);
signal slow_clk : std_logic := '0';
signal clk_divider : integer := 0;
function binary_to_seven_segment(input : std_logic_vector(3 downto 0)) return std_logic_vector is
variable seg_output : std_logic_vector(6 downto 0);
begin
case input is
when "0000" => seg_output := "1000000";
when "0001" => seg_output := "1111001";
when "0010" => seg_output := "0100100";
when "0011" => seg_output := "0110000";
when "0100" => seg_output := "0011001";
when "0101" => seg_output := "0010010";
when "0110" => seg_output := "0000010";
when "0111" => seg_output := "1111000";
when "1000" => seg_output := "0000000";
when "1001" => seg_output := "0010000";
when others => seg_output := "1111111";
end case;
return seg_output;
end function;
begin
process(clk)
begin
if rising_edge(clk) then
if clk_divider = 50000 then
slow_clk <= not slow_clk;
clk_divider <= 0;
else
clk_divider <= clk_divider + 1;
end if;
end if;
end process;
process(sw)
variable value_int : integer;
begin
value_int := to_integer(unsigned(sw));
thousands <= std_logic_vector(to_unsigned(value_int / 1000, 4));
hundreds <= std_logic_vector(to_unsigned((value_int / 100) mod 10, 4));
tens <= std_logic_vector(to_unsigned((value_int / 10) mod 10, 4));
ones <= std_logic_vector(to_unsigned(value_int mod 10, 4));
end process;
process(current_digit, ones, tens, hundreds, thousands)
begin
case current_digit is
when ones_digit => an <= "1110"; seg <= binary_to_seven_segment(ones);
when tens_digit => an <= "1101"; seg <= binary_to_seven_segment(tens);
when hundreds_digit => an <= "1011"; seg <= binary_to_seven_segment(hundreds);
when thousands_digit => an <= "0111"; seg <= binary_to_seven_segment(thousands);
when others => an <= "1111"; seg <= (others => '1');
end case;
end process;
process(slow_clk)
begin
if rising_edge(slow_clk) then
case current_digit is
when ones_digit => current_digit <= tens_digit;
when tens_digit => current_digit <= hundreds_digit;
when hundreds_digit => current_digit <= thousands_digit;
when thousands_digit => current_digit <= ones_digit;
when others => current_digit <= ones_digit;
end case;
end if;
end process;
end behavioral;

## Slide 14
VHDL arrays store multiple elements of the same type in an organized way and provide fast access
Arrays are used for grouping data, modeling multidimensional structures, and performing operations on large data sets
They serve as a foundation for creating dynamic data structures and algorithms, enabling efficient data management and simulation
Record types in VHDL allow grouping of different types of elements under a single name, where each element can have a different data type
Record types are useful for modeling complex data structures where multiple related values need to be stored together, such as a set of properties for an object
5.3 COMPOSITE TYPES

## Slide 15
Access type provides a way to point to objects
Access type allows dynamically creating objects in memory
The DEALLOCATE procedure releases allocated memory
5.4 ACCSESS TYPES
5.5 FILE TYPES
In VHDL, file types are used to define objects that represent files in the system, and the data within the file is constrained by a specific subtype
A file can be managed with operations like READ, WRITE, SEEK, and FLUSH, where the reading and writing modes determine the type of operation
type Int_Ptr is access Integer;
variable Ptr : Int_Ptr := null; -- Initially points to nothing
-------------------------------------------------------------------------
Ptr := new Integer(5); -- Creates an integer object in memory with a value of 5
-------------------------------------------------------------------------
DEALLOCATE(Ptr); -- Frees the memory and sets Ptr to null

## Slide 16
When to Use Protected Types?
When concurrent data access occurs (multiple processes need to access the same data simultaneously)
When the secure management of shared resources is required
When control and organization are necessary for data manipulation
When restricted access to critical sections is needed to ensure consistency and avoid race conditions
5.6 PROTECTED TYPES
library IEEE;
use IEEE.std_logic_1164.all;
use IEEE.numeric_std.all;
protected type sharedcounter is
procedure increment;
function getvalue return integer;
end protected;
protected body sharedcounter is
variable count: integer := 0;
procedure increment is
begin
count := count + 1;
end procedure;
function getvalue return integer is
begin
return count;
end function;
end protected body;
library IEEE;
use IEEE.std_logic_1164.all;
use IEEE.numeric_std.all;
use work.sharedcounter.all;
entity protectedtypes is
port (
clk : in std_logic;
out_counter : out integer
);
end protectedtypes;
architecture behavior of protectedtypes is
shared variable counter: sharedcounter;
begin
process(clk)
begin
if rising_edge(clk) then
counter.increment;
end if;
end process;
process(clk)
begin
if rising_edge(clk) then
out_counter <= counter.getvalue;
end if;
end process;
end behavior;
CODE EXAMPLE

## Slide 17
Why is String Representations under the types section?
Strings are a VHDL type: Defined as arrays of characters, part of the type hierarchy
Ensures type safety: Fixed or constrained strings prevent design errors
Essential for testing: Key for assertions, debugging, and messages
5.7 STRING REPRESENTATIONS
5.8 UNSPECIFIED TYPES
Unspecified types allow abstract type definitions in VHDL
They are used for generics, ports, and parameters
Types are determined during elaboration
They support scalar, array, access, and file types
These types enable flexible and reusable designs

## Slide 18
CODE EXAMPLE
library IEEE;
use IEEE.std_logic_1164.all;
use IEEE.numeric_std.all;
entity generic_adder is
generic
(
data_width : integer := 32
);
port
(
input_a : in std_logic_vector (data_width-1 downto 0);
input_b : in std_logic_vector (data_width-1 downto 0);
output_adder : out std_logic_vector (data_width downto 0)
);
end generic_adder;
architecture behavioral of generic_adder is
signal output_internal : signed (output_adder'range);
begin
output_internal <= signed(input_a) + signed(input_b);
output_adder <= std_logic_vector(output_internal);
end architecture behavioral;

## Slide 19
7.1 General
7.2 Attribute specification
7.3 Configuration specification
7.4 Disconnection specification
7. Specifications
Chapter 7
Presenter:
Furkan Kaya

## Slide 20
7.1 GENERAL
Specifications in VHDL, which define additional properties or configurations for design elements, increasing clarity, control, and customization in hardware modeling.
Associate attributes with VHDL objects to define additional properties or behaviors.
attribute PIN_NO of CIN: signal is 10;
attribute PIN_NO of COUT: signal is 5;
attribute LOCATION of ADDER1: label is (10,15);
attribute LOCATION of others: label is (25,77);
attribute CAPACITANCE of all: signal is 15 pF;
attribute IMPLEMENTATION of G1: group is "74LS152";
attribute RISING_DELAY of C2Q: group is 7.2 ns;
Define how components are bound to specific entities or architectures within a design.
use WORK.GLOBAL_SIGNALS.all;
configuration Different of Half_Adder is
for Structure
for L1: XOR_GATE
generic map (2.9 ns, 3.6 ns);
end for;
for L2: AND_GATE
generic map (2.8 ns, 3.25 ns)
port map (I2 => Tied_High);
end for;
end for;
end configuration Different;
A configuration in VHDL specifies how components within an architecture are bound to entities and architectures.
disconnect S: T after 10 ns;
disconnect others: T after 5 ms;
disconnect all: T after 273 us;
10 ns, 5 ms and 273 us are just arbitrary time expressions.
EX-1
EX-3
EX-2
7.2 ATTRIBUTE
SPECIFICATION
7.3 CONFIGURATION
SPECIFICATION
7.4 DISCONNECTION
SPECIFICATION
All of the examples are taken from "IEEE1076-2019" document.

## Slide 21
8. NAMES
8.1 General
8.2 Simple Names
8.3 Selected Names
8.4 Indexed Names
8.5 Slice Names
8.6 Attribute Names
8.7 External Names
Chapter 8
Presenter:
Orhan Çalışkan

## Slide 22
Names can include :
  Simple Name (represents a single entity)
  Operator Symbol (represent operators)
  Character Literal (represent a single character) (not in VHDL2002)
  Selected Name (provide access to an element from a package or record)
  Indexed Name (access to a specific element of an array or vector)
  Slice Name (represent a specific range of an array or vector)
  Attribute Name (represent an Attribute)
  External Name (represent an external entity) (not in VHDL2002)
8.1 GENERAL
8.2 SIMPLE NAMES
Simple names is the name you directly give to an object (signal, variable, entity, architecture, function, procedure, package etc.)

## Slide 23
Selected names access an object from within another object or from a library
  Provide modularity and readability
  Include prefix and suffix
  Selected_name ::= prefix.suffix
  IEEE.std_logic_1164.all
8.3 SELECTED NAMES
8.4 INDEXED NAMES
Indexed names used in VHDL to access specific elements of arrays.
  One index for each dimension
  Indexes must be within the bounds of the array
  indexed_name ::= prefix ( expression { , expression } )

## Slide 24
Slice name represents a segment of consecutive elements from an array
  Follows the format prefix(discrete_range)
  data(15 downto 0) -- A slice with a descending range
  data(0 to 15) -- A slice with a ascending range
  data(0 downto 15) -- A null slice
8.5 SLICE NAMES
8.6 ATTRIBUTE NAMES
Attribute name represents a value, function, type, range, signal, or constant associated with an entity
  follows the format : prefix [signature] 'attribute_designator [ (expression) ]
  clk'delayed(5 ns) -- clk signal delayed by 5 ns

## Slide 25
External name denotes an object declared in the design hierarchy containing the external name
  External Variable Name: Provides access to variables defined in other regions
  External Signal Name: Provides access to signals defined in other regions
  External Constant Name: Allows access to constants from external regions
  Package Pathname: Provides access to a specific element within a package. It is used to access elements defined within a specific package in the design
  Absolute Pathname: Starts from the root of the design and encompasses the entire hierarchy. It provides access to elements at the highest level of the design
  Relative Pathname: Accesses an element by moving up or down from the current location. It provides dynamic access based on the current position
  Partial Pathname: Refers to a specific element in more detail. It points to a particular part of the design
8.7 EXTERNAL NAMES

## Slide 26
  library IEEE;
  use IEEE.std_logic_1164.all; --This line is example for selected name
  use work.example_package.all; --This line is example for external name
  Entity my_design is --my_design is a simple name
  port
  (
  clk : in std_logic;
  rst : in std_logic;
  input_vld : in std_logic;
  comm_input : in std_logic_vector (15 downto 0); --comm_input port is a slice name
  output_vld : in std_logic;
  data_out : out std_logic_vector(15 downto 0) --data_out port is a slice name
  );
  end my_design;
  architecture behavioral of my_design is
  signal data : std_logic_vector(data_upper_lmt downto data_lower_lmt); --data is a static name
  begin
CODE EXAMPLE
  process(clk) begin
  if (clk'event and clk = '1') then --clk'event is a attribute name
  if(input_vld = '1') then
  data <= comm_input(15 downto 1) & not comm_input(0);
  --comm_input(0) is a indexed name
  end if;
  if(output_vld = '1') then
  data_out <= data;
  end if;
  end if;
  end process;

## Slide 27
14. ELABORATION AND EXECUTION
14.1 General
14.2 Elaboration of a Design Hierarchy
14.3 Elaboration of a Block, Package, Subprogram or Protected Type Header
14.4 Elaboration of a Declarative Part
14.5 Elaboration of a Statement Part
14.6 Dynamic Elaboration
14.7 Execution of a Model
Chapter 14
Presenter:
Seyit Koçak

## Slide 28
To execute a model, the design hierarchy is first elaborated, followed by the initialization of nets, and then the repetitive simulation cycle begins, during which processes are executed and nets are updated
14.1 GENERAL
14.2 ELABORATION OF A DESIGN HIERARCHY
Definition: Creates processes interconnected by nets, enabling simulation
Process:
  Executes vhpiCbStartOfElaboration and vhpiCbEndOfElaboration callbacks.Prepares block statements and implicit configurations for unbound components
Key Steps:
  Elaborates packages sequentially to resolve dependencies
  Configures PSL verification units after block elaboration
  Creates drivers and initializes scalar signals

## Slide 29
Describes the preparation of protected types, generics, subprograms, and ports, including their mapping and association. This ensures all components are properly initialized and ready for simulation
14.3 ELABORATION OF a BLOCK, PACKAGE, SUBPROGRAMS OR PROTECTED TYPE HEADER
14.4 ELABORATION OF A DECLARATIVE PART
Type definitions, subtypes, subprograms, and protected types are elaborated sequentially
. Attribute, configuration, and disconnection specifications are processed
Binding information, default values, and signal associations are properly established
14.5 ELABORATION OF A STATEMENT PART
Purpose:
  Ensure concurrent statements are correctly prepared for simulation
Concurrent Statements:
  All concurrent statements in a block are elaborated sequentially
Generate Statements:
  For-Generate: Creates blocks for each value in a specified range
  If-Generate: Creates a block if the condition evaluates to true; otherwise, no block is created
  Case-Generate: Creates a block for the matching alternative based on an evaluated expression
Component Instantiation: If bound to a design entity, the corresponding block is elaborated

## Slide 30
Definition:
  Dynamic elaboration occurs during simulation execution for constructs with sequential statements
Key Instances:
  Loop Statements: Loop parameters are elaborated, and the range is evaluated before execution
  Subprogram Calls: Parameters are elaborated and checked; exclusive access is required for protected or file operations
  Allocators: Subtype elaboration occurs before object allocation
  Sequential Blocks: Declarative parts are elaborated before block execution
14.6 DYNAMIC ELABORATION
14.7 EXECUTION OF A MODEL
Drivers: Handle signal value changes via transactions
Signal Updates: Compute and apply driving and effective values
Implicit Signals: Update signals like S'STABLE and S'QUIET per kernel rules

## Slide 31
17. VHDL Procedural Interface overview
Chapters 17, 18 and 19
Presenter:
Furkan Kaya
18. VHPI access functions
19. VHPI information model

## Slide 32
VHPI Overview
Definition: VHPI (VHDL Procedural Interface) allows interaction between external tools and the VHDL simulation environment.
Purpose:
  Extend simulation functionality.
  Provide dynamic access to design objects.
Key Components:
  Handles: Represent simulation objects (e.g., signals, entities).
  Access Functions: Perform operations on these objects.
  Callbacks: Trigger actions on specific simulation events.
Example:
vhpi_register_cb(vhpiCbValueChange, signal_handle, my_callback);

## Slide 33
VHPI Phases
Phases of Execution:
  Registration: Initialize callbacks and external tools.
  Simulation: Execute the design while interacting dynamically.
  Termination: Clean up and finalize external tool interactions.
Example:
procedure signal_monitor is
variable value: vhpiValueT;
begin
vhpi_get_value(signal_handle, value);
report "Signal value: " & value;
end;

## Slide 34
Callbacks
Example:
vhpi_register_cb(vhpiCbTime, 50 ns, my_callback);
Purpose: Dynamically respond to events during simulation.
Types of Callbacks:
  Event-based: Triggered by signal changes or processes.
  Time-based: Activated after a specific time.
  Phase-based: Executed at specific simulation phases.

## Slide 35
VHPI Data Types
Example:
signal_value: vhpiValueT;
vhpi_get_value(signal_handle, signal_value);
Definition: VHPI uses predefined data types to represent simulation data and interact with VHDL objects.
Key Data Types:
  vhpiInt: Integer type for indices and counters.
  vhpiReal: Real type for analog values or delays.
  vhpiString: Text-based data.
  vhpiValueT: Encapsulates values of signals and variables.

## Slide 36
Data Access
Example:
signal_value.format := vhpiBinStr;
signal_value.value := "1101";
vhpi_put_value(signal_handle, signal_value, vhpiForce);
Purpose: Access and manipulate data during simulation.
Methods:
  Reading values using vhpi_get_value.
  Writing values using vhpi_put_value.
  Navigating objects using handles.

## Slide 37
VHPI Object Model
Example:
signal_handle := vhpi_handle(vhpiSignal, architecture_handle);
Definition: Represents the hierarchical structure of VHDL designs, enabling navigation and manipulation of components.
Key Objects:
  Signals: Data carriers between components.
  Variables: Local storage within processes.
  Processes: Describe behavior.
  Components: Instances of entities.

## Slide 38
Object Hierarchy
Example:
root_handle := vhpi_handle(vhpiRoot, null);
entity_handle := vhpi_handle_by_name("MyEntity", root_handle);
Structure:
  Designs are organized hierarchically, starting from root objects.
  Parent-child relationships allow traversal between components.
Usage:
  Retrieve handles for signals, processes, or variables.
  Navigate design hierarchy dynamically.

## Slide 39
Signal Interaction
Example:
signal_value.value := "0000";
vhpi_put_value(signal_handle, signal_value, vhpiInertial);
Purpose: Manage signal behavior during simulation.
Actions:
  Monitor signal value changes.
  Modify signal values dynamically to simulate specific scenarios.

## Slide 40
Process and Component Interaction
Example:
process_handle := vhpi_handle(vhpiProcess, entity_handle);
vhpi_set_disable(process_handle, true);
Purpose: Interact with processes and components during runtime.
Actions:
  Activate or deactivate processes.
  Modify or monitor component behavior.

## Slide 41
Advanced Use Cases
Example:
vhpi_register_cb(vhpiCbAfter, 100 ns, my_callback);
vhpi_get_value(signal_handle, signal_value);
Applications:
  Debugging and monitoring signals.
  Automating tests with dynamic modifications.
  Interfacing with external tools for co-simulation.

## Slide 42
24. STANDARD TOOL DIRECTIVES
24.1 Protect Tool Directives
24.2 Conditional Analysis Tool Directives
Chapter 24
Presenter:
Seyit Koçak

## Slide 43
To execute a model, the design hierarchy is first elaborated, followed by the initialization of nets, and then the repetitive simulation cycle begins, during which processes are executed and nets are updated
24.1 PROTECT TOOL DIRECTIVES

## Slide 44
www.youtube.com/@falsepaths
End of IEEE 1076 – 2002 Standard
VHDL Project Closure Presentation
THANKS
Furkan Kaya,
Mert Ecevit,
Orhan Çalışkan,
Seyit Koçak
Yunus Küçük