## Slide 1: A Summary of 1076 - 2019 IEEE Standard VHDL Language Reference Manual
by Furkan Kaya, Koray Karakurt,
Mert Ecevit, Orhan Çalışkan, Seyit Koçak and Yunus Küçük
27/12/2024

## Slide 2
3.1 General
3.2 Entity Declarations
3.3 Architecture Bodies
3.4 Configuration Declarations
3. Design entities & configurations
Chapter 3
Presenter:
Furkan Kaya

## Slide 3
Design
Architecture
3.1 GENERAL
3.2 ENTITY DECLARATIONS

## Slide 4
CODE EXAMPLE
library IEEE;
use IEEE.std_logic_1164.all;
use IEEE.numeric_std.all;
entity generic_adder is
generic
(
data_width : integer := 32
);
port
(
input_a : in std_logic_vector (data_width-1 downto 0);
input_b : in std_logic_vector (data_width-1 downto 0);
output_adder : out std_logic_vector (data_width downto 0)
);
end generic_adder;
architecture behavioral of generic_adder is
signal output_internal : signed (output_adder'range);
begin
output_internal <= signed(input_a) + signed(input_b);
output_adder <= std_logic_vector(output_internal);
end architecture behavioral;

## Slide 5
4. Subprograms & packages
4.1 General
4.2 Subprogram Declarations
4.3 Subprogram Bodies
4.4 Subprogram Instantiation Declarations
4.5 Subprogram Overloading
4.6 Resolution Functions
4.7 Package Declarations
4.8 Package Bodies
4.9 Package Instantiation Declarations
4.10 Conformance Rules
Chapter 4
Presenter:
Seyit Koçak

## Slide 6
Subprograms define algorithms through procedures and functions, serving to compute values or perform actions
Procedures are subprograms that execute a series of statements to perform actions but do not return a value. They are called as statements and can modify the state of the program
Functions are classified as pure or impure
Packages separate the declarations and bodies of these subprograms, allowing common resources to be shared
4.1 GENERAL
4.2 SUBPROGRAM DECLERATİONS
Subprogram declarations define procedures or functions by specifying their designator, parameters, generics (if any), and for functions, the return type and whether it is pure or impure
Procedures are always identified by a name, while functions can also be identified by operator symbols, enabling operator overloading
Functions return a value, whereas procedures execute actions without returning any value and can modify external variables or signals
-

## Slide 7
CODE EXAMPLE
library IEEE;
use IEEE.STD_LOGIC_1164.ALL;
use IEEE.NUMERIC_STD.ALL;
procedure UpdateValue(signal clk : in STD_LOGIC; signal reset : in STD_LOGIC;
signal data_in : in STD_LOGIC_VECTOR(7 downto 0);
signal data_out : out STD_LOGIC_VECTOR(7 downto 0)) is
Begin
if reset = '1' then
data_out <= (others => '0’);
elsif rising_edge(clk) then
data_out <= data_in;
end if;
end procedure;
entity ProcedureWithClock is
Port (
clk : in STD_LOGIC;
reset : in STD_LOGIC;
data_in : in STD_LOGIC_VECTOR(7 downto 0);
data_out : out STD_LOGIC_VECTOR(7 downto 0) );
end ProcedureWithClock;
architecture Behavioral of ProcedureWithClock is
begin
process(clk, reset)
begin
UpdateValue(clk, reset, data_in, data_out);
end process;
end Behavioral;

## Slide 8
4.2 SUBPROGRAM DECLARATİONS
Pure functions always return the same output for the same input values
Impure functions may produce different outputs for the same inputs or modify external variables or signals
Constant parameters allow read-only access, while variable parameters allow both reading and writing of values during subprogram execution.
Signal parameters pass references to signals, their drivers, or both into the subprogram call Assignments to signal parameters directly affect the actual signal drivers associated with them
4.3 SUBPROGRAM BODIES
A body consists of three main parts: specification (definition of parameters and type), declarative part (variables, constants, or nested subprograms), and statement part (sequential operations)
4.4 SUBPROGRAM INSTANTIATION DECLARATIONS
Subprogram instantiation customizes a general subprogram template into an independent version with specific parameters or generics

## Slide 9
CODE EXAMPLE
library IEEE;
use IEEE.STD_LOGIC_1164.ALL;
use IEEE.NUMERIC_STD.ALL;
function Add(a, b: INTEGER) return INTEGER is
begin
return a + b;
end Add;
function Add(a, b: REAL) return REAL is
begin
return a + b;
end Add;
function PositiveAdd is new Add;
entity SubprogramInstantiationExample is
Port (
a, b : in INTEGER;
c, d : in REAL;
result_int : out INTEGER;
result_real: out REAL
);
end SubprogramInstantiationExample;
architecture Behavioral of SubprogramInstantiationExample is
constant THRESHOLD : INTEGER := 10;
begin
process(a, b, c, d)
variable tempResultInt : INTEGER;
variable tempResultReal : REAL;
begin
if (a > THRESHOLD and b > THRESHOLD) then
tempResultInt := PositiveAdd(a, b);
result_int <= tempResultInt;
else
result_int <= 0;
end if;
if (c > REAL(THRESHOLD) and d > REAL(THRESHOLD)) then
tempResultReal := Add(c, d);
result_real <= tempResultReal;
else
result_real <= 0.0;
end if;
end process;
end Behavioral;

## Slide 10
4.7,8,9 PACKAGE DECLARATIONS,BODIES,INSTANTIATION
Package declarations define the interface of a package, including constants, types, subprograms, and generics
Items declared in a package can be made visible in other design units through selection or use clauses
A package body must match its corresponding package declaration and follow it in the same declarative region
Package instantiation declarations create an instance of an uninstantiated package, associating actuals with generics through a generic map aspect
The instance behaves like a generic-mapped package with declarations and bodies from the uninstantiated package
library IEEE;
use IEEE.STD_LOGIC_1164.ALL;
package MyPackage is
constant DEFAULT_VALUE: integer := 10;
function Double(Value: integer) return integer;
function Triple(Value: integer) return integer;
end package MyPackage;
package body MyPackage is
function Double(Value: integer) return integer is
begin
return Value * 2;
end function Double;
function Triple(Value: integer) return integer is
begin
return Value * 3;
end function Triple;
end package body MyPackage;
entity PackageExample is
Port (
InputValue : in integer;
OutputValue : out integer;
TripleValue : out integer
);
end PackageExample;
architecture Behavioral of PackageExample is
use work.MyPackage.all;
begin
process(InputValue)
begin
OutputValue <= Double(InputValue);
TripleValue <= Triple(InputValue);
end process;
end Behavioral;
CODE EXAMPLE

## Slide 11
CODE EXAMPLE
library IEEE;
use IEEE.std_logic_1164.all;
use IEEE.numeric_std.all;
entity generic_adder is
generic
(
data_width : integer := 32
);
port
(
input_a : in std_logic_vector (data_width-1 downto 0);
input_b : in std_logic_vector (data_width-1 downto 0);
output_adder : out std_logic_vector (data_width downto 0)
);
end generic_adder;
architecture behavioral of generic_adder is
signal output_internal : signed (output_adder'range);
begin
output_internal <= signed(input_a) + signed(input_b);
output_adder <= std_logic_vector(output_internal);
end architecture behavioral;

## Slide 12
www.youtube.com/@falsepaths
End of IEEE 1076 – 2002 Standard
VHDL Project Closure Presentation
THANKS
Furkan Kaya,
Mert Ecevit,
Orhan Çalışkan,
Seyit Koçak
Yunus Küçük