## Slide 1
10.1 General
10.2 Wait Statement
10.3 Assertion Statement
10.4 Report Statement
10.5 Variable Assignment Statement
10.6 Procedure Call Statement
10.7 If Statement
10.8 Case Statement
10.9 Loop Statement
10.10 Next Statement
10.11 Exit Statement
10.12Return Statement
10.13 Null Statement
10.14 Sequential Block Statement
10. SEQUENTIAL STATEMENTS
Chapter 10
Presenter:
Yunus Küçük

## Slide 2: 10.1 General
Sequential statements are used to define algorithms for the execution of a subprogram or process; they execute in the order in which they appear.

## Slide 3: 10.2 WaIt Statement
There are 4 different types of wait statements which are:
  wait: it will suspend code forever.
  wait on: is equivalent to using a sensitivity list in a process. As soon as any of the signals in the wait on list changes, the code will continue to execute.
  wait until: it will suspend a process until the condition of the wait is true.
  Wait for: is never synthesizable. However, it is still very useful for test benches and for bus functional models. Wait for must be followed by some amount of time, for example 10 ns.
  One additional note: A process that has a sensitivity list can not contain any wait statements.

## Slide 4: 10.3 Assertıon statement
A statement that checks that a specified condition is true and reports an error if it is not.
Syntax:
[ label: ] assert condition [ report string_expression ] [ severity expression ];
Description:
The assertion statement has three optional fields and usually all three are used.
The condition specified in an assertion statement must evaluate to a Boolean value (true or false). If it is false, it is said that an assertion violation occurred.
The expression specified in the report clause must be of predefined type String and is a message to be reported when assertion violation occurred.
If the severity clause is present, it must specify an expression of predefined type Severity_Level, which determines the severity level of the assertion violation.
The Severity_Level type is specified in the Standard package and contains the following values: Note, Warning, Error, and Failure. If the severity clause is omitted
it is implicitly assumed to be Error.
Example:
assert not (Reset = '0' and Set = '0') report "set-reset conflict" severity Failure;
assert result = ExpectedResults report "results differ from expected results" severity Warning;
Notes:
The message is displayed when the condition is false, therefore the message should be an opposite to the condition.
The concurrent assertion statement is a passive process and as such can be specified in an entity.
The concurrent assertion statement monitors the specified condition continuously.
Synthesis tools generally ignore assertion statements.

## Slide 5: 10.4 report statement
A statement that displays a message.
Syntax:
[ label: ] report string_expression [ severity expression ];
Description:
The main difference between the report statement and the assertion statement is that the message in the report statement is displayed unconditionally.
If the severity clause is present, it must specify an expression of predefined type Severity_Level, which has the values: Note, Warning, Error, and Failure.
Example:
report "End of simulation" severity note;
Notes:
If the severity clause is omitted in a report statement it is implicitly assumed to be Note.
If the severity clause is used then the default is Error.

## Slide 6: CODE EXAMPLE of waıt statements
entity T07_WaitOnUntilTb is
end entity;
architecture sim of T07_WaitOnUntilTb is
signal CountUp : integer := 0;
signal CountDown : integer := 10;
begin
process is
begin
CountUp <= CountUp + 1;
CountDown <= CountDown - 1;
wait for 10 ns;
end process;
process is
begin
wait on CountUp, CountDown;
report "CountUp=" & integer'image(CountUp) &
" CountDown=" & integer'image(CountDown);
end process;
process is
begin
wait until CountUp = CountDown;
report "Jackpot!";
end process;
end architecture;

## Slide 7
Note: CountUp=1 CountDown=9
Time: 0 ps Iteration: 1 Process: /T07_WaitOnUntilTb/line__20 File: D:/Projects/Deneme1/Deneme1.srcs/sources_1/new/deneme.vhd
Note: CountUp=2 CountDown=8
Time: 10 ns Iteration: 1 Process: /T07_WaitOnUntilTb/line__20 File: D:/Projects/Deneme1/Deneme1.srcs/sources_1/new/deneme.vhd
Note: CountUp=3 CountDown=7
Time: 20 ns Iteration: 1 Process: /T07_WaitOnUntilTb/line__20 File: D:/Projects/Deneme1/Deneme1.srcs/sources_1/new/deneme.vhd
Note: CountUp=4 CountDown=6
Time: 30 ns Iteration: 1 Process: /T07_WaitOnUntilTb/line__20 File: D:/Projects/Deneme1/Deneme1.srcs/sources_1/new/deneme.vhd
Note: CountUp=5 CountDown=5
Time: 40 ns Iteration: 1 Process: /T07_WaitOnUntilTb/line__20 File: D:/Projects/Deneme1/Deneme1.srcs/sources_1/new/deneme.vhd
Note: Jackpot!
Time: 40 ns Iteration: 1 Process: /T07_WaitOnUntilTb/line__29 File: D:/Projects/Deneme1/Deneme1.srcs/sources_1/new/deneme.vhd
Note: CountUp=6 CountDown=4
Time: 50 ns Iteration: 1 Process: /T07_WaitOnUntilTb/line__20 File: D:/Projects/Deneme1/Deneme1.srcs/sources_1/new/deneme.vhd

## Slide 8: 10.5 varıable statement
Description:
The purpose of variables in VHDL is in cases where you need to drive outputs of a process by something that will change throughout the process,
and you need to capture each of those changes.
Notes:
Variables can only be used inside processes
Any variable that is created in one process cannot be used in another process
Variables need to be defined after the keyword process but before the keyword begin
Variables are assigned using the := assignment symbol
Variables that are assigned immediately take the value of the assignment
The most important thing to understand is that variables immediately take the value of their assignment.

## Slide 9
library ieee;
use ieee.std_logic_1164.all;
use ieee.numeric_std.all;
entity Variable_Statement is
end entity;
architecture sim of Variable_Statement is
signal MySignal : integer := 0;
begin
process
variable MyVariable : integer := 0;
begin
MyVariable := MyVariable + 1;
MySignal <= MySignal + 1;
report "MyVariable=" & integer'image(MyVariable) &
", MySignal=" & integer'image(MySignal);
wait for 10ns;
end process;
end architecture;
Note: MyVariable=1, MySignal=0
Note: MyVariable=2, MySignal=1
Note: MyVariable=3, MySignal=2
Note: MyVariable=4, MySignal=3
Note: MyVariable=5, MySignal=4
Note: MyVariable=6, MySignal=5
Note: MyVariable=7, MySignal=6
Note: MyVariable=8, MySignal=7
Note: MyVariable=9, MySignal=8
.
.
.

## Slide 10: 10.6 procedure statement
Description:
A procedure is a type of subprogram in VHDL which can help us avoid repeating code. Sometimes the need arises to perform identical operations several places throughout the design. While creating a module might be overkill for minor operations, a procedure is often what you want.
Procedures can be declared within any declarative region. The scope of the procedure will be limited to wherever it’s declared, architecture, package, or process. Whenever you call the procedure, it will behave like the code of the procedure was inserted where it was called from.
A procedure’s parameter list defines its inputs and outputs, kind of like a mini-module. It can be a signal or a constant, but unlike a module, it can also be a variable. You can declare objects between the “is” and “begin” keywords that are only valid inside the procedure. These may include constants, variables, types, subtypes, and aliases, but not signals.
Syntax:
procedure <procedure_name>
(signal|variable|constant <name1> : in|out|inout <type>;
signal|variable|constant <name2> : in|out|inout <type>;
... ) is
<declarations_for_use_within_the_procedure>
begin
<code_performed_by_the_procedure_here>
end procedure;

## Slide 11: 10.7 ıf statement
Description:
An if statement selects for execution one or none of the enclosed sequences of statements, depending on the value of one or more corresponding conditions.
Syntax:
if_label : if condition then
sequence_of_statements
elsif condition then
sequence_of_statements
else
sequence_of_statements
end if;

## Slide 12
entity If_Statement is
end entity;
architecture sim of If_Statement is
signal CountUp : integer := 0;
signal CountDown : integer := 10;
begin
process is
begin
CountUp <= CountUp + 1;
CountDown <= CountDown - 1;
wait for 10 ns;
end process;
process is
begin
if CountUp > CountDown then
report "CountUp is larger";
elsif CountUp < CountDown then
report "CountDown is larger";
else
report "They are equal";
end if;
wait on CountUp, CountDown;
end process;
end architecture;
Note: CountDown is larger
Time: 0 ps Iteration: 0
Note: CountDown is larger
Time: 0 ps Iteration: 1
Note: CountDown is larger
Time: 10 ns Iteration: 1
Note: CountDown is larger
Time: 20 ns Iteration: 1
Note: CountDown is larger
Time: 30 ns Iteration: 1
Note: They are equal
Time: 40 ns Iteration: 1
Note: CountUp is larger
Time: 50 ns Iteration: 1
Note: CountUp is larger
Time: 60 ns Iteration: 1
Note: CountUp is larger
Time: 70 ns Iteration: 1
Note: CountUp is larger
Time: 80 ns Iteration: 1
Note: CountUp is larger
Time: 90 ns Iteration: 1
Note: CountUp is larger
Time: 100 ns Iteration: 1
Note: CountUp is larger

## Slide 13: 10.8 case statement
Syntax:
case <expression> is
when <choice> =>
code for this branch
when <choice> =>
code for this branch
...
end case;
Description:
The VHDL Case Statement works exactly the way that a switch statement in C works. Given an input, the statement looks at each possible condition to find one that the input signal satisfies. They are useful to check one input signal against many combinations.
Just like in C, the VHDL designer should always specify a default condition provided that none of the case statements are chosen. This is done via the “when others =>” statement. See the code below for an example of this.

## Slide 14
library ieee;
use ieee.std_logic_1164.all;
use ieee.numeric_std.all;
entity Case_Statementis
end entity;
architecture sim of Case_Statementis
signal Sig1 : unsigned(7 downto 0) := x"AA";
signal Sig2 : unsigned(7 downto 0) := x"BB";
signal Sig3 : unsigned(7 downto 0) := x"CC";
signal Sig4 : unsigned(7 downto 0) := x"DD";
signal Sel : unsigned(1 downto 0) := (others => '0');
signal Output1 : unsigned(7 downto 0);
begin
-- Stimuli for the selector signal
process is
begin
wait for 10 ns;
Sel <= Sel + 1;
wait for 10 ns;
Sel <= Sel + 1;
wait for 10 ns;
Sel <= Sel + 1;
wait for 10 ns;
Sel <= Sel + 1;
wait for 10 ns;
Sel <= "UU";
wait;
end process;
-- Equivalent MUX using a case statement
process(Sel, Sig1, Sig2, Sig3, Sig4) is
begin
case Sel is
when "00" =>
Output2 <= Sig1;
when "01" =>
Output2 <= Sig2;
when "10" =>
Output2 <= Sig3;
when "11" =>
Output2 <= Sig4;
when others => -- 'U', 'X', '-', etc.
Output2 <= (others => ‘0');
end case;
end process;
end architecture;

## Slide 15: 10.9 loop statement
Syntax:
for <name> in <lower_limit> to <upper_limit> loop
<statement>;
<statement>;
end loop;
while <condition> loop
<statement>;
<statement>;
end loop;

## Slide 16
library ieee;
use ieee.std_logic_1164.all;
use ieee.std_logic_unsigned.all;
use ieee.numeric_std.all;
entity Loop_Statement is
end entity;
architecture sim of Loop_Statement is
begin
for_process : process is
begin
for i in 1 to 10 loop
report "i = " & integer'image(i);
end loop;
wait;
end process;
while_process : process is
variable j : integer := 0;
begin
while j < 10 loop
report "j = " & integer'image(j);
j := j + 2;
end loop;
wait;
end process;
end architecture;

## Slide 17: 10.10 next statement
The next statement is used to complete execution of one of the iterations of an enclosing loop statement, making it jump back to the top of that loop. The completion is conditional if the statement includes a condition.
Syntax:
[ label: ] next [ loop_label ] [ when condition ];
Description:
The next statement allows to skip a part of an iteration loop. If the condition specified after the when reserved word is true, or if there is no condition at all, then the statement is executed. This results in skipping all statements below it until the end of the loop and passing the control to the first statement in the next iteration.
A next statement may specify the name of the loop it is expected to influence. If no label is supported then the statement applies to the innermost enclosing loop.
Note:
The next statement is often confused with the exit statement. The difference between the two is that the exit statement "exits" the loop entirely, while the next statement skips to the "next" loop iteration.
L1: loop
k:= 0;
L2: for CountValue in 1 to 8 loop
next when CountValue = N; -- jump to next itteration of loop L2
if A(k):= 'U' then
next L1; -- jump to top of loop L1
end if;
k:= k + 1;
end loop L2;
end loop L1;

## Slide 18: 10.11 Exıt statement
A sequential statement which is used to finish or exit the execution of an enclosing loop statement.
Syntax:
[ label: ] exit [ loop_label ] [ when condition ];
Description:
The exit statement terminates entirely the execution of the loop in which it is located. If a condition is placed on the exit statement, then the execution of the exit statement depends on the condition placed at the end of the statement. When the condition is true (or if there is no condition at all) the exit statement is executed and the control is passed to the first statement after the end loop.
Example:
L1: loop
L2: for I in 0 to 7 loop
if B(I) = 'U' then
exit L1;
end if;
exit when I = M;
end loop L2;
...
end loop L1;
Note:
The exit statement is often confused with the next statement. The difference between the two is that the exit statement "exits" the loop entirely, while the next statement skips to the "next" loop iteration (in other words, "exits" only the current iteration of the loop).

## Slide 19: 10.12 Return statement
The return statement is used to complete the execution of the innermost enclosing function or procedure body.
Syntax:
[ label: ] return [ expression ];
Description :
The return statement ends the execution of a subprogram (procedure or function) in which it appears. It causes an unconditional jump to the end of the subprogram.
The return statement is only allowed in a procedure or function body. The return statement in a procedure may not return any value, while a return in a function must return a value consistent with the return type of the function.
Example:
return X + Y;

## Slide 20: 10.13 null statement
A null statement performs no action.
Syntax:
[ label : ] null ;
Description:
The execution of the null statement has no effect other than to pass on to the next statement.