Section 8 : Names

Section 8.1 General

Names in VHDL are used to define objects, values, methods, or attributes and can be explicitly or implicitly declared.

Types of names: Simple names, selected names, indexed names, slices, and attribute names.

Prefix: Can be a name or a function call. If the prefix is a function call, it refers to an element, slice, or attribute of the function result.

Static names: Fully determined during compilation, such as an array with a fixed index.

Non-static names: Contain values that can change over time, like an index defined by a signal.

Static prefix: The longest static part of a non-static name.

Ambiguous names cause compilation errors. Using null access values in function calls is invalid.

- Examples:
  - array(2) is static
  - array(index) is dynamic
  - record.element is a selected name.

Section 8.2 Simple Name

- Simple name in VHDL is an identifier that refers to an entity, configuration, package, procedure, function, or architecture as defined in their declaration. It serves only to identify the entity without any additional effects.
- Alias in VHDL is a shorthand or alternative name for an existing object, such as a signal, variable, type, or subprogram. It allows easier access or more descriptive naming for parts of a design.

Section 8.3 Selected Name

- Selected name in VHDL is used to reference a named entity defined
  - In another named entity : record, package etc.
  - In a design library

Selected name fallows the syntax : selected_name ::= prefix.suffix

  - Prefix, Indicates the container (e.g., a library, package, record, or access type).
  - Suffix, Indicates the specific item (e.g., a field in a record, all elements in a package).

Section 8.4 Indexed Names

- indexed name denotes an element of an array.
  - indexed_name ::= prefix ( expression { , expression } )

Section 8.5 Slice Names

Slice name refers to a subset of consecutive elements from a one-dimensional array. It is defined by a prefix (the array) and a discrete range (the index range). The slice can have an ascending or descending range, and it inherits the base type of the array.

Section 8.6 Attribute Names

In VHDL, attribute names are used to access specific properties of named entities, such as signals, constants, or types. They provide useful details like the size of an array, the left most index of an array, or the path of a signal.
  - Predefined Attributes: These include attributes like 'LEFT, 'PATH_NAME, and 'DELAYED, which return details like the leftmost index of an array, the path of a signal, or a delayed signal value.

  - Aliases: Attributes can also be used with aliases. The alias refers to the attributes of the original entity.

  - Function Attributes: These attributes return values based on functions, such as the size of an array.

Section 8.7 External Names

External name refers to an object declared in a design hierarchy. It can represent a constant, signal, or variable declared outside the current scope but within a reachable region. The object is identified by an external pathname, which can be an absolute, relative, or package pathname. An external name allows referencing external constants, signals, or variables in VHDL designs, ensuring that objects can be accessed from different parts of the design hierarchy. If an object does not match the specified type or is not found in the designated region, it results in an error.

Section 12 : Scope and Visibility

Section 12.1 Declerative Region

  - Declarative region defines where a declaration (signal, variable, function, etc.) is valid.
In nested regions, the innermost region takes precedence.

Structures Treated as a Single Declarative Region
- Entity + Architecture
- Subprogram (Function/Procedure)
- Package (Declaration + Body)
- Process, Loop, Block, Generate
- Record and Protected Types

Root Declerative Region
- Encompasses the fundamental units of a design.
- Contains no declarations initially.

Library Declerative Region
- Each library forms its own declarative region.
- Units within the library are accessible from this region.

Continuity of Text
The declaration and its body, even if separated in the text, are considered part of the same declarative region.

Section 12.2 Scope of Declerations

Scope Definition
The scope of a declaration is the part of the code where its name (signal, variable, constant, etc.) is valid.

Immediate Scope
A declaration is valid within its enclosing block or region.

Extended Scope
Some declarations, such as package contents, generics, and ports, extend beyond their immediate scope into configurations or library usage.

Library and Configuration Scope
Declarations in libraries or configurations can extend their scope to other parts of the design using use clauses or configurations.

Section 12.3 Visibility
Direct Visibility:
A declaration is directly visible within its immediate scope unless it is hidden by a homograph in an inner scope.
Visibility by Selection:
A declaration is visible through selection when referenced using a prefix (e.g., library name, package name, or hierarchical name).
Hidden Visibility:
A declaration is hidden if a homograph exists in an inner scope or due to specific rules (e.g., subprograms hiding their own names or predefined operations being overridden).
Extended Visibility:
Visibility extends to configurations and block configurations under certain conditions, such as use clauses or associations in port and generic mappings.

Section 12.4 Use Clauses
The use clause in VHDL is used to make specific declarations from a package or library visible in the current design unit's scope. It allows selecting individual declarations or all declarations (use <package_name>.all). The visibility starts immediately after the use clause and extends to the end of the current declarative region. However, a declaration may be hidden by homographs (declarations with the same name) within the same scope. Explicit declarations take precedence over implicit ones, and the use clause cannot make declarations from an uninstantiated package visible.

Section 12.5 The Context of Overload Resolution
Overload resolution determines the correct interpretation of overloaded entities (such as names, subprograms, or operator symbols) when multiple meanings are possible due to visibility rules. It considers all visible declarations, and the occurrence is legal only if there is exactly one interpretation in the context. The rules applied during overload resolution include syntax, scope, visibility, and type compatibility, among others. For overloaded subprograms, the resolution also takes into account parameter types and result types.

Section 13 : Design Units and Their Analysis

Section 13.1 Design Units

In VHDL design, there are two main types of design units: primary units, such as entity, package, configuration, and context, and secondary units, such as architecture and package body. Each design unit is analyzed independently and stored in a design library, where naming rules ensure uniqueness. Specifically, each primary unit within the same library must have a unique name, and every architecture associated with a given entity must also have a unique name to avoid conflicts.
A critical component of design units is the context clause, which specifies the required libraries and packages. However, for context declarations, the context clause must remain empty. Additionally, secondary units, such as architecture, are always linked to their corresponding primary units, such as entity, and this relationship is verified during the analysis process.
These rules ensure proper organization, reusability, and error-free compilation of VHDL designs, making them fundamental for successful hardware description.

Section 13.2 Design Libraries

In VHDL, design libraries store analyzed units and are categorized into working libraries (for storing units) and resource libraries (referenced during analysis). Libraries are defined using a library clause like library ieee, work;. The STD and WORK libraries are implicitly included in each design unit. Logical names like STD refer to specific libraries, and secondary units must be placed in the same library as their corresponding primary units, ensuring proper organization.

Section 13.3 Context Decleration

Context declaration is used to define library and use clauses that can be reused across design units. The name in the declaration must be the same at both the beginning and the end. Additionally, it is an error to define or reference the WORK library within a context. This structure helps maintain clean and reusable code.

Section 13.4 Context Clauses
Context clauses in VHDL define the environment (libraries and visibility rules) in which a design unit is analyzed. They consist of library clauses, use clauses, and context references.
Library clauses specify logical library names to be referenced.
Use clauses make specific declarations visible within the design unit.
Context references refer to other context declarations and expand their contents (libraries and use clauses) into the current context.

Section 13.5 Order of Analysis
A primary unit referenced in a design unit must be analyzed before the design unit itself.
A secondary unit must be analyzed after its corresponding primary unit.
If an error occurs during the analysis of a design unit, the analysis is rejected and does not affect the current working library.
A library unit is affected by changes in any referenced library unit.
A secondary unit is affected by changes in its primary unit.
If a library unit is changed (e.g., through reanalysis), all dependent units become obsolete and must be reanalyzed before use.

Section 15 : Design Units and Their Analysis
Section 15.2 Character Set

The basic character set is sufficient for writing any description.
The usable characters are same the VHDL2002.

Section 15.3 Lexical elements, separators, and delimiters
Lexical Elements:
Includes delimiters, identifiers (reserved words included), literals (abstract, character, string, or bit-string), comments, and elements defined for tool directives or PSL (Property Specification Language).
PSL (Property Specification Language) is a formal language defined in IEEE Std 1850 used to describe the behavior and properties of hardware designs. It enables specifying and verifying functional requirements, often in simulation or formal verification tools. PSL is compatible with multiple hardware description languages (e.g., VHDL, Verilog) and ensures a design meets its intended specifications.
The delimiter is either one of the special characters(VHDL2019) :

The delimiter is either one of the special characters(VHDL2002) :

The compound delimiter is either one of the special characters(VHDL2019) :

The compound delimiter is either one of the special characters(VHDL2002) :

Section 15.4 Identifiers
In VHDL 2019, an identifier is a name used to represent objects like variables, signals, constants, processes, or entities. It must follow these rules:
Basic Identifiers:
Start with a letter (A-Z, a-z)
Contain only letters, digits (0-9),and underscores (_)
Cannot end with an underscore or have consecutive underscores
Reserved keywords cannot be used
Extended Identifiers:
Enclosed in backslashes (\) for special characters or reserved keywords
Can include spaces, symbols, or VHDL keywords
Case sensitive (\Signal\ ≠ \SIGNAL\)

Section 15.5 Abstract Literals

In VHDL-2019, abstract literals are general numerical expressions that are independent of type and are converted to an appropriate data type based on context.
- Decimal literals include integers and floating-point numbers in base 10.
- Based literals are written in a format specifying a base and value but support only integer values.

Section 15.6 Character Literals

In VHDL, a character literal represents a single character enclosed in single quotes (') and can include any of the 191 printable ASCII characters, such as letters, digits, symbols, the space, and the nonbreaking space. The single quote character itself is represented as ''''. Character literals belong to the character type and are used to define single characters in constants, variables, or signals.

Section 15.7 String Literals

In VHDL, a string literal is a sequence of characters enclosed in double quotes (").
To include a double quote inside, use two adjacent double quotes ("").
The length is the number of characters, counting doubled quotes as one.
String literals are used for messages, text processing, or initializing character arrays.

Section 15.8 Bit String Literals

A bit string literal in VHDL is a sequence of characters enclosed in quotation marks, preceded by a base specifier (e.g., B, O, X) and optionally an integer specifying the length.
 It represents a bit value with digits (0-1 for binary, 0-7 for octal, 0-F for hexadecimal) and may include underscores for readability.
The base specifier determines how the digits are interpreted (binary, octal, hexadecimal, etc.).
The value of a bit string literal is a string formed from the bit value, removing underscores and expanding the bits as needed.

Section 15.9 Comments

In VHDL, comments can be single-line (--) or delimited (/* ... */).
Comments do not affect the validity of the VHDL description and are used solely for documentation purposes.

Section 15.10 Reserved Words

List of reserved words that were introduced in VHDL-2019, which are not part of VHDL-2002:

procedural
Introduced for more control over processes and procedural aspects in VHDL-2019. It provides additional flexibility when defining and managing procedural blocks.

reference
Added in VHDL-2019 to work with reference types. It allows for referencing objects or data structures directly without copying, improving memory management and performance, particularly for complex data types.

vmode, vprop, vunit
These are simulation-related keywords introduced in VHDL-2019, allowing greater flexibility for specifying simulation modes, properties, and units of measurement.

Section 23 : VHPI Function Reference

Section 23.1 General

VHPI functions define the required arguments, the operations they perform, and the results they return. These functions typically return a pointer to a string or a structure.

The returned data can be either permanent or transient. Permanent data is securely stored in memory and can be referenced later using a pointer. Transient data, however, is preserved only until the next call to the same function or until the control thread returns to the tool, after which it may be overwritten.

If transient data is needed for a longer period, the VHPI program must copy the data. Additionally, strings are represented as null-terminated character arrays. These details are critical for understanding and correctly implementing the data management rules of VHPI functions.

Section 23.2 vhpi_assert

The vhpi_assert function is used to report error messages, similar to the report statement in VHDL. The severity argument specifies the severity level of the error, while formatmsg defines the message content using the C printf format.

The function returns 0 if it executes successfully or 1 if an error occurs. If the severity level is critical, such as VHPI_FAILURE, the simulation may stop.

vhpi_assert(VHPI_FAILURE, "Error: Signal 'clk' is not '1'.");
This function makes it easier to detect and report errors during simulation.

Section 23.3 vhpi_check_error

The vhpi_check_error function checks if the previous VHPI function call raised an error. If an error occurred, it returns error information in the structure pointed to by the error_info_p argument. This structure includes details such as the error severity, message, associated VHDL source file and line number, and other implementation-specific information.
If no error occurred, the function returns 0. If an error occurred and error_info_p is not NULL, the error information is written into the structure, and the function returns 1. The memory for the error information structure must be allocated by the VHPI program before calling the function.

int vhpi_check_error(vhpiErrorInfoT *error_info_p);
This function checks if the previous VHPI function call resulted in an error. It fills a provided vhpiErorInfoT structure with error details if an error occurred, or returns 0 if no error occurred.

Section 23.4 vhpi_compare_handles

The vhpi_compare_handles function compares two VHPI handles (handle1 and handle2) to check if they refer to the same object. Since handles may have different representations, the == operator cannot be used for comparison.

The vhpi_compare_handles function returns 1 if the two handles refer to the same object, and 0 if they refer to different objects.