Section 8 : Names

Section 8.1 General

Names in VHDL are used to define objects, values, methods, or attributes and can be explicitly or implicitly declared.

Types of names: Simple names, selected names, indexed names, slices, and attribute names.

Prefix: Can be a name or a function call. If the prefix is a function call, it refers to an element, slice, or attribute of the function result.

Static names: Fully determined during compilation, such as an array with a fixed index.

Non-static names: Contain values that can change over time, like an index defined by a signal.

Static prefix: The longest static part of a non-static name.

Ambiguous names cause compilation errors. Using null access values in function calls is invalid.

- Examples:
  - array(2) is static
  - array(index) is dynamic
  - record.element is a selected name.

Section 8.2 Simple Name

- Simple name in VHDL is an identifier that refers to an entity, configuration, package, procedure, function, or architecture as defined in their declaration. It serves only to identify the entity without any additional effects.
- Alias in VHDL is a shorthand or alternative name for an existing object, such as a signal, variable, type, or subprogram. It allows easier access or more descriptive naming for parts of a design.

Section 8.3 Selected Name

- Selected name in VHDL is used to reference a named entity defined
  - In another named entity : record, package etc.
  - In a design library

Selected name fallows the syntax : selected_name ::= prefix.suffix

  - Prefix, Indicates the container (e.g., a library, package, record, or access type).
  - Suffix, Indicates the specific item (e.g., a field in a record, all elements in a package).

Section 8.4 Indexed Names

- indexed name denotes an element of an array.
  - indexed_name ::= prefix ( expression { , expression } )

Section 8.5 Slice Names

Slice name refers to a subset of consecutive elements from a one-dimensional array. It is defined by a prefix (the array) and a discrete range (the index range). The slice can have an ascending or descending range, and it inherits the base type of the array.

Section 8.6 Attribute Names

In VHDL, attribute names are used to access specific properties of named entities, such as signals, constants, or types. They provide useful details like the size of an array, the left most index of an array, or the path of a signal.
  - Predefined Attributes: These include attributes like 'LEFT, 'PATH_NAME, and 'DELAYED, which return details like the leftmost index of an array, the path of a signal, or a delayed signal value.

  - Aliases: Attributes can also be used with aliases. The alias refers to the attributes of the original entity.

  - Function Attributes: These attributes return values based on functions, such as the size of an array.

Section 8.7 External Names

External name refers to an object declared in a design hierarchy. It can represent a constant, signal, or variable declared outside the current scope but within a reachable region. The object is identified by an external pathname, which can be an absolute, relative, or package pathname. An external name allows referencing external constants, signals, or variables in VHDL designs, ensuring that objects can be accessed from different parts of the design hierarchy. If an object does not match the specified type or is not found in the designated region, it results in an error.

Section 12 : Scope and Visibility

Section 12.1 Declerative Region

  - Declarative region defines where a declaration (signal, variable, function, etc.) is valid.
In nested regions, the innermost region takes precedence.

Structures Treated as a Single Declarative Region
- Entity + Architecture
- Subprogram (Function/Procedure)
- Package (Declaration + Body)
- Process, Loop, Block, Generate
- Record and Protected Types

Root Declerative Region
- Encompasses the fundamental units of a design.
- Contains no declarations initially.

Library Declerative Region
- Each library forms its own declarative region.
- Units within the library are accessible from this region.

Continuity of Text
The declaration and its body, even if separated in the text, are considered part of the same declarative region.

Section 12.2 Scope of Declerations

Scope Definition
The scope of a declaration is the part of the code where its name (signal, variable, constant, etc.) is valid.

Immediate Scope
A declaration is valid within its enclosing block or region.

Extended Scope
Some declarations, such as package contents, generics, and ports, extend beyond their immediate scope into configurations or library usage.

Library and Configuration Scope
Declarations in libraries or configurations can extend their scope to other parts of the design using use clauses or configurations.

Section 12.3 Visibility
Direct Visibility:
A declaration is directly visible within its immediate scope unless it is hidden by a homograph in an inner scope.
Visibility by Selection:
A declaration is visible through selection when referenced using a prefix (e.g., library name, package name, or hierarchical name).
Hidden Visibility:
A declaration is hidden if a homograph exists in an inner scope or due to specific rules (e.g., subprograms hiding their own names or predefined operations being overridden).
Extended Visibility:
Visibility extends to configurations and block configurations under certain conditions, such as use clauses or associations in port and generic mappings.

Section 12.4 Use Clauses
The use clause in VHDL is used to make specific declarations from a package or library visible in the current design unit's scope. It allows selecting individual declarations or all declarations (use <package_name>.all). The visibility starts immediately after the use clause and extends to the end of the current declarative region. However, a declaration may be hidden by homographs (declarations with the same name) within the same scope. Explicit declarations take precedence over implicit ones, and the use clause cannot make declarations from an uninstantiated package visible.

Section 12.5 The Context of Overload Resolution
Overload resolution determines the correct interpretation of overloaded entities (such as names, subprograms, or operator symbols) when multiple meanings are possible due to visibility rules. It considers all visible declarations, and the occurrence is legal only if there is exactly one interpretation in the context. The rules applied during overload resolution include syntax, scope, visibility, and type compatibility, among others. For overloaded subprograms, the resolution also takes into account parameter types and result types.